| XXIII MEETING OF PERMANENT CONSULTATIVE COMMITTEE II: RADIOCOMMUNICATIONS March 17 to 21, 2014 Cartagena de Indias, Colombia | OEA/Ser.L/XVII.4.2 CCP.II-RADIO/doc. 3469/14 24 February 2014 Original: English |
| --- | --- |
|  | AGENDA ITEM 1.1 ( 1 435- 1 525 MHz Band): PRELIMINARY PROPOSAL FOR WRC-15 |  |
|  | (Item on the Agenda: 3.1 (SGT1)) |  |
|  | (Document submitted by the delegation of the United States of America) |  |

Agenda Item 1.1:to consider additional spectrum allocations to the mobile service on a primary basis and identification of additional frequency bands for International Mobile Telecommunications (IMT) and related regulatory provisions, to facilitate the development of terrestrial mobile broadband applications, in accordance with Resolution 233 (WRC-12)

Background Information:  The band 1435 MHz – 1525 MHz (and subsets of the band) have been identified as “suitable frequency ranges” for IMT; they have also been addressed in sharing studies conducted within Joint Task Group JTG 4-5-6-7 in preparation for the 2015 World Radio Conference.  The band has been and continues to be used widely in the United States and other Region 2 Administrations for aeronautical mobile telemetry (i.e. “AMT,” or “flight test”).

The 1435 – 1525 MHz band is essential for aerospace research and development, and for the certification of aircraft prior to commercial use. Interference-free, real-time use of the band is essential to the protection of test aircraft, payloads, flight crews, and persons and property located beneath flight test airspace.  The continued use of the band 1435 - 1525 MHz on an interference-free basis is essential for the aerospace manufacturing industries and their many suppliers in Region 2, including Administrations in both North and South America.

Based on the studies introduced to date in the JTG, AMT sharing of the band with interference- limited IMT services has been demonstrated as infeasible. The studies concluded independently that co-frequency operation of AMT and IMT operations requires exclusion zones in excess of100 km with respect to interference from IMT to AMT ground stations, and over 350 km for interference from AMT aircraft to IMT systems on the ground.  The latter distance is measured with respect to the flight test ground station that is supervising the flight test aircraft.  Flight test aircraft routinely fly several hundred kilometers in all directions from their AMT ground stations.  This extends the impact of signals from aircraft transmitters to IMT users to distances that are well beyond the radio line of sight from the IMT user to the AMT ground station.

Radio Regulation 5.343 prescribes that “In Region 2, the use of the band 1435-1535 MHz by the aeronautical mobile service for telemetry has priority over other uses by the mobile service.”

The United States proposes to retain this foot note in Region 2 in order to protect the flight safety aspects of AMT operations from domestic and cross-border interference.

RR 5.343 is important for the avoidance of cross-border interference to and from flight test operations in Region 2.  The footnote does not preclude administrations from implementing any mobile service systems within their own territories; rather, it ensures that in sensitive border areas administrations take proper account of long-established AMT operations.

For the foregoing reasons, the 1435 – 1535 MHz band should not be identified for IMT use in Region 2.

Proposal:

ARTICLE5

Frequency allocations

Section IV – Table of Frequency Allocations 
(See No. 2.1)

NOC	USA/1.1/1

1 300-1 525 MHz

| Allocation to Services |
| --- |
| Region 1 | Region 2 | Region 3 |
| … | 1 429-1 452 FIXED MOBILE 5.343 5.338A 5.341 |
| … | 1 452-1 492 FIXED MOBILE 5.343 BROADCASTING BROADCASTING-SATELLITE 5.208B 5.3415.344 5.345 |
| … | 1 492-1 518 FIXED MOBILE 5.343 5.3415.344 | ... |
| … | 1 518-1 525 FIXED MOBILE 5.343 MOBILE-SATELLITE (space-to-Earth) 5.3485.348A 5.348B 5.351A 5.3415.344 | ... |

Reason:  Based on studies submitted in ITU-R, co-frequency sharing between IMT and AMT is not practical, and therefore the band 1435-1525 MHz should not be identified for IMT use in Region 2.

NOC	USA/1.1/2

1 525-1 610 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 1 525-1 530 SPACE OPERATION (space-to-Earth) FIXED MOBILE-SATELLITE (space-to-Earth) 5.208B5.351A Earth exploration-satellite Mobile except aeronautical mobile 5.349 | 1 525-1 530 SPACE OPERATION (space-to-Earth) MOBILE-SATELLITE (space-to-Earth) 5.208B5.351A Earth exploration-satellite Fixed Mobile 5.343 | 1 525-1 530 SPACE OPERATION (space-to-Earth) FIXED MOBILE-SATELLITE (space-to-Earth) 5.208B5.351A Earth exploration-satellite Mobile 5.349 |
| 5.3415.3425.3505.351 5.352A5.354 | 5.3415.3515.354 | 5.3415.3515.352A5.354 |
| 1 530-1 535 SPACE OPERATION (space-to-Earth) MOBILE-SATELLITE (space-to-Earth) 5.208B5.351A5.353A Earth exploration-satellite Fixed Mobile except aeronautical mobile | 1 530-1 535 SPACE OPERATION (space-to-Earth) MOBILE-SATELLITE (space-to-Earth) 5.208B5.351A5.353A Earth exploration-satellite Fixed Mobile 5.343 |
| 5.3415.3425.3515.354 | 5.3415.3515.354 |
| … |

Reason:  Based on studies submitted in ITU-R, co-frequency sharing between IMT and AMT is not practical, and therefore the band 1525-1535 MHz should not be identified for IMT use in Region 2.

# Footnotes

See JTG 4-5-6-7/ Docs 156 (July 2013)and4-5-6-7/291 (October 2013)