| IX MEETING OF PERMANENT CONSULTATIVE COMMITTEE II: RADIOCOMMUNICATIONS INCLUDING BROADCASTING April 17 to 20, 2007 San Salvador, El Salvador | OEA/Ser.L/XVII.4.2 CCP.II-RADIO/doc.1403/07 rev.2 4 May 2007 Original: English |
| --- | --- |
|  | DRAFT INTER-AMERICAN PROPOSALS FOR WORKING SUB-GROUP 3 OF THE WORKING GROUP FOR THE PREPARATION FOR WRC-07 |  |
|  | (Item on the Agenda: 4.1) |  |
|  | (Document submitted by the Coordinator) |  |

Table of Contents

STRUCTURE OF WSG-3	2

Agenda item 1.12	3

Proposal for Agenda item 1.12:  Power flux-density limits for the 27.5 GHz band	3

Proposal for Agenda item 12:  Appendix 5 Coordination arc in the band 17.3-17.8 GHz and other closely related proposals	4

Proposal for Agenda item 12:  No. 11.47	14

Proposal for Agenda item 12:  Provisions of RR No. 22.2	16

Proposal for Agenda item 1.12:  Appendix 7 Table 10 for ground-based earth stations and aircraft terrestrial stations	17

Proposal for Agenda item 1.12:  RR Appendix 4 data element (C.8.d.2) contiguous satellite bandwidth	19

Proposal for Agenda item 1.12:  Resolution 88 (WRC-03)	20

Proposal for Agenda item 1.12:  Coordination of the radionavigation-satellite service (space-to-space) in the bands 1 215-1 300 MHz and 1 559-1 610 MHz	21

Proposal for Agenda item 1.12:  Provisions of RR No. 11.49	23

Proposal for Agenda item 1.12:  Provisions of RR No. 9.1	23

Proposal for Agenda item 1.12:  Resolution 86 (WRC-03)	25

Proposal for Agenda item 1.12:  Application of the provisions of RR No. 9.14	25

Proposal for Agenda item 1.12:  Nos. 9.15 to 9.18	26

Proposal for Agenda item 1.12: Non-Payment of Satellite Network Cost Recovery for Notification	27

Agenda item 2:	33

Proposal for Agenda item 2:  Recommendation ITU-R M.541	34

Proposal for Agenda item 2:  Recommendation ITU-R P.833	34

Proposal for Agenda item 2:  Recommendation ITU-R M.1174	35

Proposal for Agenda item 2:  Recommendation ITU-R M.1642	36

Proposals for Agenda item 2:  References to ITU-R Recommendations in the Radio Regulations requiring modification to bring them into accordance with Resolution 27 (Rev.WRC-03) (Annex 2, No. 5)	36

Proposals for Agenda item 2:  Incorporation by reference of ITU-R Recommendations mentioned in WRC Resolutions	41

Proposals for Agenda item 2:  ITU-R Recommendations incorporated by reference in the Radio Regulations which have been revised and approved since WRC-03	42

Agenda item 4	48

Proposal for Agenda item 4:  Resolution 33 (Rev. WRC-03)	48

STRUCTURE OF WSG-3

| Agenda items | Coordinator | Coordinator Alternate |
| --- | --- | --- |
| 1.1, 1.12, 2, 3, 4, 5, 6, 7.1 | Julie Zoller United States of America julie.zoller@itt.com | Javier Garcia Dominican Republic jgarcia@indotel.org.do |

| Agenda item | Rapporteur | Rapporteur Alternate |
| --- | --- | --- |
| 1.1 | Javier García Dominican Republic jgarcia@indotel.org.do | Diego Merino Cadena Ecuador dmerino@conatel.gov.ec |
| 1.12 | Chantal Beaumier Canada Beaumier.chantal@ic.gc.ca Flavio da Silva Brazil fdasilva@loralskynet.com | Glenn Feldhake United States of America glenn.s.feldhake@nasa.gov Héctor Budé Eastern Republic of Uruguay hbude@ursec.gub.uy |
| 2 | Héctor Budé Eastern Republic of Uruguay hbude@ursec.gub.uy | Javier García Dominican Republic jgarcia@indotel.org.do |
| 3 | Audrey Allison United States of America audrey.allison@boeing.com |  |
| 4 | Javier García Dominican Republic jgarcia@indotel.org.do | Leslie Green Eastern Republic of Uruguay lgreen@ursec.gub.uy |
| 5 | Audrey Allison United States of America audrey.allison@boeing.com | Rafael Sanchez Dominican Republic rsanchez@indotel.org.do |
| 6 | Audrey Allison United States of America audrey.allison@boeing.com |  |
| 7.1 | Chantal Beaumier Canada Beaumier.chantal@ic.gc.ca | Leslie Green Eastern Republic of Uruguay lgreen@ursec.gub.uy |

Agenda item 1.12

To consider possible changes in response to Resolution 86 (Rev. Marrakesh, 2002) of the Plenipotentiary Conference: “Advance publication, coordination, notification and recording procedures for frequency assignments pertaining to satellite networks” in accordance with Resolution 86 (WRC-03).

## Proposal for Agenda item 1.12:  Power flux-density limits for the 27.5 GHz band

Background information

The last sentence of RR No. 5.538 makes reference to the application of pfd limits contained in Table 21-4 of RR Article 21 in the band 27.500-27.501 GHz whereas Table 21-4 does not contain this frequency band.

It is proposed to modify Table 21-4 and No. 5.538 as shown in Section 6/1.12/1.4 of the CPM Report.

MOD 		DIAP/1.12/1

Support: Canada, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

TABLE 21-4 (continued) (wrc-07)

| Frequency band | Service* | Limit in dB(W/m2) for angles of arrival () above the horizontal plane | Reference bandwidth |
| --- | --- | --- | --- |
|  |  | 0-5 | 5-25 | 25-90 |  |
| ... |  |  |  |  |  |
| 19.3-19.7 GHz 22.55-23.55 GHz 24.45-24.75 GHz 25.25-27.5 GHz 27.500-27.501 GHz | Fixed-satellite (space-to-Earth) Earth exploration-satellite (space-to-Earth) Inter-satellite Space research (space-to-Earth) | –115 | –115 + 0.5( – 5) | –105 | 1 MHz |

MOD 		DIAP/1.12/2

Support: Canada, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

5.538	Additional allocation: the bands 27.500-27.501 GHz and 29.999-30.000 GHz are also allocated to the fixed-satellite service (space-to-Earth) on a primary basis for the beacon transmissions intended for up-link power control. Such space-to-Earth transmissions shall not exceed an equivalent isotropically radiated power (e.i.r.p.) of 10 dBW in the direction of adjacent satellites on the geostationary-satellite orbit.

Reasons:  To incorporate the power flux-density limits in the band 27.500-27.501 GHz in Table 21-4 of Article 21 and delete the corresponding reference in RR No. 5.538.

## Proposal for Agenda item 12:  Appendix 5 Coordination arc in the band 17.3-17.8 GHz and other closely related proposals

Background information

Resolution 901 (WRC-03) invites ITU-R “to conduct studies on the applicability of the coordination arc concept for space radiocommunication services not yet covered by these Regulations” as well as “to recommend, as appropriate, the orbital separation required for triggering inter-service and intra-service coordination concerning the satellite services in frequency bands above 3.4 GHz for geostationary-satellite (GSO) networks not subject to a Plan and not already covered by the coordination arc concept specified in No. 9.7 (GSO/GSO) of Table 5-1 (Appendix 5), under items 1), 2) and 3) of the frequency band column, and subject to Section II of Article 9”.  This Resolution further resolves to recommend that a future competent conference review the results of ITU-R studies on the application of the coordination arc and consider including the results of these studies in Appendix 5.  Review of such study results are considered under Resolution 86 of Agenda item 1.12.

Pursuant to Resolution 901, ITU-R studied the appropriate coordination arc value to trigger coordination between Broadcasting-Satellite Service (BSS) networks serving Region 2 in the band 17.3-17.8 GHz and Fixed Satellite Service (FSS) (space-to-Earth) networks serving Region 1 in the band 17.3-17.7 GHz and FSS (space-to-Earth) networks serving Regions 1, 2 and 3 in the band 17.7-17.8 GHz.

The ITU-R studies concluded that a coordination arc value of ±8° is appropriate to trigger coordination between GSO BSS networks serving Region 2 and GSO FSS (space-to-Earth) networks whose service areas are limited to Region 1 in the band 17.3-17.7 GHz and between GSO BSS networks serving Region 2 and GSO FSS (space-to-Earth) networks whose service areas are limited to Regions 1 and/or 3 in the band 17.7-17.8 GHz.  As a result, specific changes are proposed to Table 5-1 of Appendix 5 to incorporate these conclusions.  For the case of Region 2 FSS (space-to-Earth) with respect to Region 2 BSS in the 17.7 – 17.8 GHz band footnote No. 5.517 applies.

5.517	In Region 2, the allocation to the broadcasting-satellite service in the band 17.3-17.8 GHz shall come into effect on 1 April 2007. After that date, use of the fixed-satellite (space-to-Earth) service in the band 17.7-17.8 GHz shall not claim protection from and shall not cause harmful interference to operating systems in the broadcasting-satellite service.

Changes to the wording of this provision, as well as consequential changes to the Table of Allocations are proposed recognizing that the 1 April 2007 date has passed.

Finally, also for Region 2, No. 5.518 applies for the Mobile Service.

5.518	Different category of service:  in Region 2, the allocation of the band 17.7-17.8 GHz to the mobile service is on a primary basis until 31 March 2007.

Suppression of this provision is proposed, recognizing that the 31 March 2007 date has passed.

Propuestas

MOD 		DIAP/1.12/3

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

Appendix 5 (Rev.WRC-07)

Identification of administrations with which coordination is to be effected or 
agreement sought under the provisions of Article 9

TABLE  5-1     (Rev.WRC-037)

Technical conditions for coordination
(see Article 9)

| Reference of Article 9 | Case | Frequency bands (and Region) of the service for which coordination is sought | Threshold/condition | Calculation method | Remarks |
| --- | --- | --- | --- | --- | --- |
| No. 9.7 GSO/GSO | A station in a satellite network using the geostationary-satellite orbit (GSO), in any space radiocommunication service, in a frequency band and in a Region where this service is not subject to a Plan, in respect of any other satellite network using that orbit, in any space radiocommunication service in a frequency band and in a Region where this service is not subject to a Plan, with the exception of the coordination between earth stations operating in the opposite direction of transmission | 1) 3 400-4 200 MHz 5 725-5 850 MHz (Region 1) and 5 850-6 725 MHz 7 025-7 075 MHz | i) Bandwidth overlap, and ii) any network in the fixed-satellite service (FSS) and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of ( 10° of the nominal orbital position of a proposed network in the FSS |  | With respect to the space services listed in the threshold/condition column in the bands in 1), 2), 3), 4) and 5), 6) and 7) an administration may request, pursuant to No. 9.41, to be included in requests for coordination, indicating the networks for which the value of (T/T calculated by the method in § 2.2.1.2 and 3.2 of Appendix 8 exceeds 6%. When the Bureau, on request by an affected administration, studies this information pursuant to No. 9.42, the calculation method given in § 2.2.1.2 and 3.2 of Appendix 8 shall be used |
|  |  | 2) 10.95-11.2 GHz 11.45-11.7 GHz 11.7-12.2 GHz (Region 2) 12.2-12.5 GHz (Region 3) 12.5-12.75 GHz (Regions 1 and 3) 12.7-12.75 GHz (Region 2) and 13.75-14.5 GHz | i) Bandwidth overlap, and ii) any network in the FSS or broadcasting-satellite service (BSS), not subject to a Plan, and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of ( 9° of the nominal orbital position of a proposed network in the FSS or BSS, not subject to a Plan |  |  |

TABLE  5-1 (CONTINUED)     (Rev.WRC-037)

| Reference of Article 9 | Case | Frequency bands (and Region) of the service for which coordination is sought | Threshold/condition | Calculation method | Remarks |
| --- | --- | --- | --- | --- | --- |
| No. 9.7 GSO/GSO (cont.) |  | 3) 17.7-20.2 GHz, (Regions 2 and 3), 17.3-20.2 GHz (Region 1) and 27.5-30 GHz | i) Bandwidth overlap, and ii) any network in the FSS and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of ( 8° of the nominal orbital position of a proposed network in the FSS |  |  |
|  |  | 4) 17.3-17.7 GHz (Regions 1 and 2) | i) Bandwidth overlap, and ii) a) any network in the FSS and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of ( 8° of the nominal orbital position of a proposed network in the BSS or b) any network in the BSS and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of ( 8° of the nominal orbital position of a proposed network in the FSS |  |  |
|  |  | 5) 17.7-17.8 GHz | i) Bandwidth overlap, and ii) a) any network in the FSS and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of ( 8° of the nominal orbital position of a proposed network in the BSS or any network in the BSS and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of ( 8° of the nominal orbital position of a proposed network in the FSS (See also No. 5.517) |  |  |
|  |  | 46) Bands above 17.3 GHz, except those defined in § 3) | i) Bandwidth overlap, and ii) any network in the FSS and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of (8° of the nominal orbital position of a proposed network in the FSS (see also Resolution 901 (WRC-03)) |  |  |
|  |  | 57) Bands above 17.3 GHz, except those defined in § 4) and 5 | i) Bandwidth overlap, and ii) any network in the FSS or BSS, not subject to a Plan, and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of (16° of the nominal orbital position of a proposed network in the FSS or BSS, not subject to a Plan, except in the case of a network in the FSS with respect to a network in the FSS (see also Resolution 901 (WRC-03)) |  |  |

TABLE  5-1 (CONTINUED)     (Rev.WRC-037)

| Reference of Article 9 | Case | Frequency bands (and Region) of the service for which coordination is sought | Threshold/condition | Calculation method | Remarks |
| --- | --- | --- | --- | --- | --- |
| No. 9.7 GSO/GSO (cont.) |  | 68) All frequency bands, other than those in 1), 2), 3), 4) and , 5), 6) and 57), allocated to a space service, and the bands in 1), 2), 3), 4) and, 5), 6) and 57) where the radio service of the proposed network or affected networks is other than the space services listed in the threshold/condition column, or in the case of coordination of space stations operating in the opposite direction of transmission | i) Bandwidth overlap, and ii) Value of T/T exceeds 6% | Appendix 8 | In application of Article 2A of Appendix 30 for the space operation functions using the guardbands defined in § 3.9 of Annex 5 of Appendix 30, the threshold/condition specified for the FSS in the bands in 2) applies. In application of Article 2A of Appendix 30A for the space operation functions using the guardbands defined in § 3.1 and 4.1 of Annex 3 of Appendix 30A, the threshold/condition specified for the FSS in the bands in 4) applies |

Reasons:  These modifications to Table 5-1 of Appendix 5 incorporate the results of ITU-R studies that conclude that a coordination arc of ±8º between Region 2 BSS and Regions 1&3 FSS in the bands 17.3-17.8 GHz is sufficient for triggering coordination between these services.  These modifications also note that No. 5.517 applies in the band 17.7-17.8 GHz.

NOC 	DIAP/ 1.12/4

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

RESOLUTION 901 (WRC-03)

Determination of the orbital arc separation for which coordination would be required between two satellite networks operating in a space 
service not subject to a Plan

Reason:  The study called for in this Resolution is still valid for other cases not yet addressed by the ITU-R

Other Closely Related Proposals for Modifying the Table of Allocations

MOD 	DIAP/1.12/5

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

5.517	In Region 2, the allocation to the broadcasting-satellite service in the band 17.3-17.8 GHz shall come into effect on 1 April 2007. After that date, use of the fixed-satellite (space-to-Earth) service in the band 17.7-17.8 GHz shall not claim protection from and shall not cause harmful interference to operating systems in the broadcasting-satellite service.

Reasons:  Modifications to this footnote are consequential to the 1 April 2007 date having passed.

SUP 	DIAP/ 1.12/6

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

Reasons:   Suppression of this RR provision is consequential to the 31 March 2007 date having passed.

MOD 	DIAP/ 1.12/7

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

15.4-18.4 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 17.3-17.7 FIXED-SATELLITE (Earth-to-space) 5.516 (space-to-Earth) 5.516A 5.516B Radiolocation | 17.3-17.7 FIXED-SATELLITE (Earth-to-space) 5.516 BROADCASTING-SATELLITE Radiolocation | 17.3-17.7 FIXED-SATELLITE (Earth-to-space) 5.516 Radiolocation |
| 5.514 | 5.514 5.515 | 5.514 |
| 17.7-18.1 FIXED FIXED-SATELLITE (space-to-Earth) 5.484A (Earth-to-space) 5.516 MOBILE | 17.7-17.8 FIXED FIXED-SATELLITE (space-to-Earth) (Earth-to-space) 5.516 BROADCASTING-SATELLITE Mobile 5.515 MOD 5.517 | 17.7-18.1 FIXED FIXED-SATELLITE (space-to-Earth) 5.484A (Earth-to-space) 5.516 MOBILE |

Reasons:  Modifications to the table are consequential to the modifications made to the wording of No. 5.517 and the suppression of No. 5.518.

## Proposal for Agenda item 12:  No. 11.47

Background information

WRC-03 identified in Resolution 86 (WRC-03) the scope and the criteria to be used for the implementation of Resolution 86 (Rev. Marrakesh, 2002).  Resolves 1) of Resolution 86 (WRC-03) specifically states that WRC-07 should “consider any proposals which deal with deficiencies in the advance publication, coordination, notification and recording procedures of the Radio Regulations for space services which have either been identified by the Board and included in the Rules of Procedure or which have been identified by administrations or by the Bureau as appropriate.”  WRC-03 also resolved that future WRCs consider any proposals that are intended to transform the content of the Rules of Procedure into regulatory text.

WRC-03 modified No. 11.44 by suppressing the possibility of extension of the date of bringing into use. However, WRC-did not modify the provisions of No. 11.47 which still refers to an “extension granted under No. 11.44”. In light of this decision, ITU-R has concluded that these provisions should be amended in order to be consistent with the decision taken by WRC-03 on No. 11.44.

In addition, No. 11.47 states that “Any frequency assignment provisionally recorded under this provision shall be brought into use by the date specified in the notice …” It has been noted that the date of bringing into use specified in the notice is an anticipated date, subject to change. The Rule of Procedure (RoP) on No. 11.47 addresses the procedures to be followed by the Radiocommunication Bureau (BR) when the responsible administration fails to notify the bringing into use of provisionally recorded assignments by the date recorded in the Master Register.  This RoP provides the notifying administration with the possibility to modify this expected date of bringing into use without any justification, as long as the new date falls within the limits prescribed in No. 11.44. It should, therefore, be recognized that the assignment should not be cancelled if it is not brought into use by the expected date of bringing into use, but only the non-respect of the 7-year period should lead to cancellation.

No. 11.47 also refers to the provisional recording of assignments to terrestrial stations, as it mentions the extension provided under No. 11.45. ITU-R has concluded that no change should be made in this area.

# Proposal

This proposal modifies the provisions of No. 11.47 to suppress the reference to any extension granted under No. 11.44, consistent with the decisions of WRC-03 to modify No. 11.44. It is also proposed to remove the requirement to bring into use assignments to space stations provisionally recorded in the Master Register by the date specified in the notice, as this date is considered as an expected date of bringing into use and the only regulatory deadline is the latest date provided by No. 11.44. Under this approach, it is proposed that the Bureau send a reminder only when the administration fails to advise the Bureau that the provisionally recorded assignment has been brought into use in accordance with No. 11.44. It is further proposed that, with these modifications, the RoP associated with No. 11.47 can be suppressed.

Finally, it is proposed not to amend the provisions of No. 11.47 in respect of terrestrial services.  It is proposed to modify No. 11.47 as shown in Section 6/1.12/4 of the CPM Report.]

MOD 		DIAP/ 1.12/ 8

Support: Canada, United States of America

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

11.47		All frequency assignments notified in advance of their being brought into use shall be entered provisionally in the Master Register. Any frequency assignment to a space station provisionally recorded under this provision shall be brought into use no later than the end of the period provided under No. 11.44. Any other frequency assignment provisionally recorded under this provision shall be brought into use by the date specified in the notice, or by the extension granted under No. 11.45, as the case may be. Unless the Bureau has been informed by the notifying administration of the bringing into use of the assignment, it shall, no later than fifteen days before the notified date of bringing into use, in the case of an earth station, or the end of the regulatory period established under No. 11.44 or No. 11.45, as appropriate, send a reminder requesting confirmation that the assignment has been brought into use within the regulatory period. If the Bureau does not receive that confirmation within thirty days following the notified date of bringing into use, in the case of an earth station, or the period provided under No. 11.44 or No. 11.45, as the case may be, it shall cancel the entry in the Master Register. The Bureau shall inform the administration concerned before taking such action.

Reasons:

1)	To address the inconsistency created with the modification of No. 11.44 at WRC-03;

2)	To remove the regulatory nature associated with the notified date of bringing into use assignments provisionally recorded in the Master Register;

3)	To incorporate the associated rules of procedure outlining the actions to be taken by the Bureau and the filing administration should the Bureau not be advised that assignments provisionally recorded in the Master Register  have been brought into use by the latest date prescribed by Nos. 11.44 or 11.45 as applicable;

- To reduce the administrative burdens on the BR in managing this process.

## Proposal for Agenda item 12:  Provisions of RR No. 22.2

Background information

RR No. 22.2 is the provision that governs the sharing between non-geostationary satellite (non-GSO) systems vis-à-vis geostationary satellite (GSO) networks in the fixed-satellite service (FSS) and the broadcasting-satellite service (BSS), except when it is explicitly disabled through a footnote in RR Article 5 through a Resolution adopted by a World Radiocommunication Conference (WRC). In the light of the decisions taken by the last WRCs, clarification may be needed concerning the respective status of non-GSO systems and GSO networks in cases where RR No. 22.2 applies.  It is proposed to modify No. 22.2 in accordance with text of Section 6/1.12/5 of the CPM Report.

Proposal

MOD 		DIAP/1.12/9

Support: Canada, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

22.2	§ 2	1)	Non-geostationary-satellite systems shall not cause unacceptable interference to or claim protection from geostationary-satellite networks in the fixed-satellite service and the broadcasting-satellite service operating in accordance with these Regulations. No. 5.43A does not apply in this case.     (WRC-07)

Reasons:  To clarify that NGSO systems shall not claim protection from GSO networks.  The last sentence referring to the non-application of No. 5.43A is required in order to avoid any inconsistency between the operational nature of No. 22.2 which refers to the notion of unacceptable interference (level to be agreed between the administrations concerned taking into account, inter alia, footnote A.22.1) and the regulatory nature of No. 5.43A (implicitly applicable unless otherwise specified because of the occurrence of the words “nor claim protection from”) which refers to the notion of harmful interference.

## Proposal for Agenda item 1.12:  Appendix 7 Table 10 for ground-based earth stations and aircraft terrestrial stations

Background information

Resolution 86 (Rev. Marrakesh, 2002) requested that WRC-03 and subsequent Conferences review the regulatory procedures associated with the advance publication, coordination, notification and recording of frequency assignments pertaining to satellite network. WRC-03 identified in Resolution 86 (WRC-03) the scope and the criteria to be used for the implementation of Resolution 86 (Rev. Marrakesh, 2002).  Resolves 1 of Resolution 86 (WRC-03) specifically states that WRC-07 should “consider any proposals which deal with deficiencies in the advance publication, coordination, notification and recording procedures of the Radio Regulations (RR) for space services which have either been identified by the Board and included in the Rules of Procedure or which have been identified by administrations or by the Bureau as appropriate.”

A review of Appendix 7, Table 10 (Predetermined coordination distance) indicates that the case of ground-based earth stations and aircraft terrestrial stations, except for those specifically identified cases in the table, is missing.  In the past the Radiocommunications Bureau has used the predetermined distance of 500 km for this case, e.g., see Document RRB98/134(Rev.1) dated 8 December 1998.  This coordination distance was derived assuming line-of-sight propagation between the aircraft and ground-based stations with a 4/3 Earth radius and the aircraft altitude of 12 km.  The 500 km is consistent with the distance currently applicable to the similar cases of coordination between aircraft and ground-based stations such as i) ground-based earth stations in the bands below 1 GHz to which No. 9.11A applies/ground-based mobile in the bands within the range 1-3 GHz to which No. 9.11A applies and aircraft (mobile) terrestrial stations; ii) aircraft (mobile) earth stations and ground-based terrestrial stations; and iii) non-GSO MSS feeder-link earth stations and aircraft (mobile) terrestrial stations.  To cover the case of ground-based earth stations and aircraft terrestrial stations, Table 10 needs to be modified to include this case with a coordination distance of 500 km.  The proposal does not apply to frequency bands already covered in Table 10.

Proposals

MOD 	DIAP/1.12 /10

Support: Canada, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

APPENDIX 7

TABLE  10     (WRC-03)

Predetermined coordination distances

| Frequency sharing situation | Coordination distance (in sharing situations involving services allocated with equal rights) (km) |
| --- | --- |
| Type of earth station | Type of terrestrial station |  |
| Ground-based | Mobile (aircraft) (all bands not included elsewhere in Table 10) | 500 |

Reasons:	For No. 9.17, this modification is needed to cover the case of ground-based earth stations and aircraft terrestrial stations.

## Proposal for Agenda item 1.12:  RR Appendix 4 data element (C.8.d.2) contiguous satellite bandwidth

Background information

WRC-03 reviewed Annex 2 of RR Appendix 4. Among the modifications, WRC-03 added an item C.8.d.2 “Contiguous satellite bandwidth”. This item was introduced in RR Appendix 4 in order to cover the specific cases where a transmitting satellite transponder would operate in a multi-carrier mode, where the aggregate bandwidth of the transmitted carriers would be different and lower than the transponder bandwidth.

This item was introduced in RR Appendix 4 in order to help administrations to conduct coordination in these cases of multi-carrier transmissions. The relationship between this item and item C.3.a “Bandwidth of the assigned frequency band” is considered here.  It is proposed to modify Appendix 4 as shown in Section 6/1.12/7 of the CPM Report

Proposals

MOD 		DIAP/1.12/11

Support: Canada, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

Appendix  4  (Rev.WRC-07)

Consolidated list and tables of characteristics for use in the
application of the procedures of Chapter III

MOD 		DIAP/1.12/12

Support: Canada, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

ANNEX 2

Characteristics of satellite networks, earth stations 
or radio astronomy stations     (WRC-07)

MOD 	DIAP/1.12/13

Support: Canada, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

Reasons:  To modify Annex 2 to RR Appendix 4, in order to request the submission of item C.8.d.2 only if it is different from the item C.3.a.

## Proposal for Agenda item 1.12:  Resolution 88 (WRC-03)

Background information

Resolution 88 (WRC-03) resolves that WRC-07 review the results of studies to be undertaken by the ITU-R on the rationalization of RR Articles 9 and 11, taking due account of RR No. 0.3, and take appropriate action.  It is proposed to suppress Resolution 88 (WRC-03) as shown in Section 6/1.12/8 of the CPM Report.

Proposals

SUP 	DIAP/1.12/14

Support: Canada, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

RESOLUTION  88  (WRC-03)

Rationalization of Articles 9 and 11 of the Radio Regulations

Reasons: Suppression of Resolution 88 (WRC-03) is appropriate because of the potential disadvantages from rationalization of Articles 9 and 11 of the Radio Regulations.

## Proposal for Agenda item 1.12:  Coordination of the radionavigation-satellite service (space-to-space) in the bands 1 215-1 300 MHz and 1 559-1 610 MHz

Background information

The scope and criteria to be used for the implementation of Resolution 86 (Rev. Marrakesh, 2002) of the Plenipotentiary Conference by future world radiocommunication conferences (WRCs) is established in Resolution 86 (WRC-03). Resolves 1 of Resolution 86 (WRC-03) relates to the consideration of proposals dealing with deficiencies in the advance publication, coordination and notification procedures of the Radio Regulations for space services, and Resolves 2 relates to consideration of proposals intended to transform the content of the Rules of Procedure into regulatory text.

WRC-2000 added the space-to-space direction to the existing radionavigation-satellite service (RNSS) (space-to-Earth) allocations in the bands 1 215-1 300 MHz and 1 559-1 610 MHz, along with footnote 5.329A. WRC-03 added footnote 5.328B, which applied coordination between two non-GSO RNSS systems and between non-GSO and GSO RNSS systems in the bands 1 164-1 300 MHz, 1 559-1 610 MHz and 5 010-5 030 MHz under Nos. 9.12, 9.12A and 9.13 after 1 January 2005, without specifying direction (i.e., space-to-Earth or space-to-space).  Coordination between GSO RNSS systems in the same bands (space-to-Earth and space-to-space) is covered by No. 9.7, again without specifying direction (i.e., space-to-Earth or space-to-space).

No. 9.11A applies the coordination provisions of Nos. 9.12 to 9.16 where the requirement to coordinate is included in a footnote to the Table of Frequency Allocations referring to No. 9.11A.  Since WRC-2000, the Rules of Procedure (RoP), issued by the Radio Regulations Board (RRB), rather than the Radio Regulations have defined the services and frequency bands for which the coordination procedure under No. 9.11A is required. The RRB considered the application of No. 9.11A to the bands given in No. 5.329A (i.e., 1 215-1 300 and 1 559-1 610 MHz) and interpreted the Regulations as excluding RNSS (space-to-space) assignments in the bands given in No. 5.329A from any obligation to coordinate with other services and with RNSS (space-to-Earth), but as obliging these RNSS (space-to-space) assignments to coordinate with each other.

In addition, many RNSS (space-to-space) network assignments are receive-only in the bands 1215-1 300 MHz and 1 559-1 610 MHz. Resolution 610 (WRC-03), as referenced in No. 5.328B, requires administrations to provide evidence of binding agreements for the manufacture, procurement, and launch of RNSS systems and networks. This resolution was intended to aid bilateral coordination between transmitting RNSS systems and networks by ensuring such systems are either in operation or in the process of being implemented.  Requiring Resolution 610 (WRC-03) data for receiving space stations is unnecessary.

Therefore, modifications to No. 5.329A and No. 5.328B are needed to reflect the RRB decision that requires RNSS (space-to-space) to coordinate only with other RNSS (space-to-space) but not with other services or with RNSS (space-to-Earth), and to remove Resolution 610 (WRC-03) obligations from RNSS receiving space stations.  Additionally, to ensure that the obligation on RNSS (space-to-space) networks under No. 5.329A is also adequately reflected for geostationary RNSS (space-to-space) networks with respect to GSO RNSS (space-to-Earth) networks in the 1215-1300 MHz and 1559-1610 MHz bands (a coordination scenario not encompassed by Nos. 9.12, 9.12A, and 9.13), the modification to No. 5.328B refers as well to No. 9.7.

Proposals

MOD 		DIAP/ 1.12 /15

Support: Canada, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

5.328B	The use of the bands 1 164-1 300 MHz, 1 559-1 610 MHz and 5 010-5 030 MHz by systems and networks in the radionavigation-satellite service for which complete coordination or notification information, as appropriate, is received by the Radiocommunication Bureau after 1 January 2005 is subject to the application of the provisions of Nos. 9.12, 9.12A and 9.13. Resolution 610 (WRC-03) shall also apply; however, in the case of radionavigation-satellite service (space-to-space) networks and systems, Resolution 610 (WRC-03) shall only apply to transmitting space stations. In accordance with No. 5.329A, for systems and networks in the radionavigation-satellite service (space-to-space) in the bands 1 215-1 300 MHz and 1 559-1 610 MHz the provisions of Nos. 9.7, 9.12, 9.12A and 9.13 shall only apply with respect to other systems and networks in the radionavigation-satellite service (space-to-space).     (WRC-07)

Reasons:  To make it clear that the application of the coordination procedure in Nos. 9.7, 9.12, 9.12A and 9.13 to RNSS (space-to-space) systems and networks is only with respect to other radionavigation-satellite service (space-to-space) systems and networks  in the bands 1 215-1 300 MHz and 1 559-1 610 MHz and to limit the application of Resolution 610 (WRC-03) to transmitting space stations.

MOD 		DIAP/ 1.12 /16

Support: Canada, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

5.329A	Use of systems in the radionavigation-satellite service (space-to-space) operating in the bands 1 215-1 300 MHz and 1 559-1 610 MHz is not intended to provide safety service applications, and shall not impose any additional constraints on radionavigation-satellite service (space-to-Earth) systems or on other services operating in accordance with the Table of Frequency Allocations.     (WRC-07)

Reasons:  To clarify that “other systems” in No. 5.329A refers to the radionavigation-satellite service (space-to-Earth) and that “services” refers to services other than the radionavigation-satellite service.

## Proposal for Agenda item 1.12:  Provisions of RR No. 11.49

Background information

The provisions of RR No. 11.49 are mainly applied by administrations in the case of malfunction of a satellite and allow the continuation of the rights of the assignment to be protected. ITU-R has concluded that two years, as provided in RR No. 11.49, is the appropriate period for the malfunctioning spacecraft to be replaced to allow for actual situations.

Proposals

NOC 	DIAP/1.12/17

Support: Canada, United States of America

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

11.49

Reasons:	ITU-R has concluded that two years, as provided in RR No. 11.49, is the appropriate period for the malfunctioning spacecraft to be replaced to allow for actual situations and that there should be no changes in the provisions of RR No. 11.49.

## Proposal for Agenda item 1.12:  Provisions of RR No. 9.1

Background information

There has been a longstanding requirement in Article 9 of the Radio Regulations, under No. 9.1, for the Radiocommunications Bureau to wait a requisite six months after receiving the advanced publication information for satellite networks requiring coordination under Section II of Article 9 before receiving the accompanying coordination request information, even if both sets of information are submitted to the Bureau at the same time.  While this six-month delay may have served a purpose in years past when there was a substantial amount of technical data included in the API for administrations to consider and potentially comment upon, this is no longer the case.  As a consequence of the simplification of the Radio Regulations at WRC-95, the API for satellite networks requiring coordination under Section II of Article 9 includes very limited information, e.g. orbital position and frequency bands, and as such, there is little for administrations to review and comment upon.  In addition, this six month delay has the effect of adding uncertainty into the possible availability of orbital slots, as conflicting coordination requests associated with other, earlier filed APIs, may be received by the BR during the six month period thereby making a previously available orbital slot no longer available.  This required six month delay therefore serves no purpose other than to delay the overall coordination process for satellite networks and add uncertainty as to the possible availability of orbital slots.

Proposals

MOD    	DIAP/1.12/18

Support: Brazil, Canada, Dominican Republic, United States of America

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

9.1		Before initiating any action under this Article or under Article 11 in respect of frequency assignments for a satellite network or a satellite system, an administration, or one9 acting on behalf of a group of named administrations, shall, prior to the coordination procedure described in Section II of Article 9 below, where applicable, send to the Bureau a general description of the network or system for advance publication in the International Frequency Information Circular (BR IFIC) not earlier than seven years and preferably not later than two years before the planned date of bringing into use of the network or system (see also No. 11.44). The characteristics to be provided for this purpose are listed in Appendix 4. The coordination or notification information may also be communicated to the Bureau at the same time. When coordination is required by Section II of Article 9, the coordination information shall be considered as having been received by the Bureau upon the date of receipt of the complete information. Where coordination is not required by Section II, notification shall be considered as having been received by the Bureau not earlier than six months after the date of publication of the advance publication information.     (WRC-07)

Reasons: To address the unnecessary requirement for the Radiocommunications Bureau to wait six months after receipt of the advanced publication information before receiving the coordination request information for satellite networks requiring coordination under Section II of Article 9.

## Proposal for Agenda item 1.12:  Resolution 86 (WRC-03)

Background information

Resolution 86 (Rev. Marrakesh, 2002) deals with the review and update of the various procedures (advance publication, coordination, notification and recording in the MIFR) for frequency assignments pertaining to satellite networks. This Resolution was initially adopted by PP-98 after an in-depth review of these procedures was conducted by the VGE (Voluntary Group of Experts) and induced profound modifications in the RR. The main purpose of this Resolution is to invite the WRCs to review and update the various steps in the regulatory procedures for space networks/systems.

PP-02 modified this Resolution by settling the global framework of the review of the space procedures, including aspects related to equitable access to the orbit/spectrum resource and to cost savings in BR and the administrations. PP-02 also invited WRC-03 to determine the scope and criteria to be used for the implementation of this Resolution.

In response to this invitation, WRC-03 adopted Resolution 86 (WRC-03) which contains the various criteria to be used in the context of the corresponding WRC Agenda item.  The 2006 Plenipotentiary Conference considered modifying Resolution 86 (Rev. Marrakesh, 2002) and concluded not to change that Resolution due to the disagreement on the scope of modification. However, PP-06 decided to invite WRC-07 to consider the matter further and report to PP-10.

Proposals

NOC		DIAP/1.12/19

Support: Brazil, Canada

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

RESOLUTION  86  (WRC-03)

Scope and criteria to be used for the implementation of 
Resolution 86 (Rev. Marrakesh, 2002) of the 
Plenipotentiary Conference

Reasons:  As stated in view B in Section 6/1.12/14.2 of the CPM Report, the framework provided by Resolution 86 (WRC-03) is satisfactory and it should be retained.

## Proposal for Agenda item 1.12:  Application of the provisions of RR No. 9.14

Background information

The Rule of Procedure on RR No. 9.14 specifies that “No. 9.14 applies to space-to-Earth frequency allocations only, i.e. coordination of a transmitting space station in respect of receiving terrestrial stations when the threshold value is exceeded. In the absence of threshold value, the provisions of No. 9.50.1 could apply (see also Appendix 5)”.

Considering that this Rule has not raised difficulties and can be translated in RR text, it is proposed to amend the wording of RR No. 9.14 to reflect the Rule of Procedure. Consequently, the Rules of Procedure on RR No. 9.14 related to this aspect should be suppressed.

Proposals

MOD 	DIAP/1.12/20

Support: Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

9.14	i)	for a transmitting space station of a satellite network for which the requirement to coordinate is included in a footnote to the Table of Frequency Allocations referring to this provision or to No. 9.11A in respect of receiving stations of terrestrial services where the threshold value is exceeded;     (WRC-07)

Reasons:	To reflect the Rule of Procedure on No. 9.14, as shown in Section 6/1.12/15 of the CPM Report.

## Proposal for Agenda item 1.12:  Nos. 9.15 to 9.18

Background information

Since WRC-95, with the consideration and adoption of the report of the Voluntary Group of Experts (VGE), at various WRCs several attempts have been made to merge RR No. 9.15 into RR No. 9.17 and RR No. 9.16 into RR No. 9.18 due to the apparent similarity of these two pairs of provisions. In fact RR No. 9.15 and RR No. 9.16 stem from former Resolution 46 (WARC-92) and RR No. 9.17 and RR No. 9.18 stem from former provisions RR1107 and RR1148 (Edition of 1990). However, after lengthy discussion, these different WRCs have recognized that the objectives and purposes of the two pairs mentioned above were entirely different.

The merging of these two pairs would thus cause unforeseeable difficulties. Incorporation/merging of provisions of RR No. 9.15 with RR No. 9.17 and provisions of RR No. 9.16 with RR No. 9.18 is not consistent with the letter and the spirit of the Radio Regulations. Such incorporation/merging does not simplify the application of these provisions and may create confusion for administrations in applying these provisions.

ITU-R has concluded that no change be made to these provisions.

Proposals

NOC 		DIAP/1.12/21

Support: Canada, United States of America

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

9.15 to 9.18

Reasons:	Nos. 9.15 to 9.18 of the Radio Regulations address different coordination procedures and should remain without change as stated in Section 6/1.12/16 of the CPM Report.

## Proposal for Agenda item 1.12: Non-Payment of Satellite Network Cost Recovery for Notification

Background information

WRC 2000, as a result of including the consequences of non-payment of cost recovery fees, modified footnotes in Article 9, Appendices 30, 30A, and 30B.  These footnotes provided that if payments were not received in accordance with the provisions as set forth in Decision 482, as modified,  the Bureau would cancel the publication, after informing the administration concerned.  Council 05 approved a further modified Decision 482, which extended satellite network cost recovery requirements to notifications of satellite network filings.  As a result of this action, similar modifications are required for Article 11, Appendices 30, 30A and 30B.

Proposals

MOD 		DIAP/1.12/22

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

Article 11

Notification and recording of frequency assignments1, 2, 3, 4, 5, 6     (WRC-07)

Section II  –  Examination of notices and recording of frequency assignments

in the Master Register

Reasons:  Consequential editorial change.

MOD 		DIAP/1.12/23

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

11.28	Complete notices shall be marked by the Bureau with their date of receipt and shall be examined in the date order of their receipt. On receipt of a complete notice the Bureau shall, within no more than two months, publish10A its contents, with any diagrams and maps and the date of receipt, in the BR IFIC which shall constitute the acknowledgement to the notifying administration of receipt of its notice. When the Bureau is not in a position to comply with the time limit referred to above, it shall periodically so inform the administrations, giving the reasons therefore.

Reasons:  Add a footnote to point to new footnote 11.28.1 which takes into account satellite network cost recovery requirements for notification.

ADD 		DIAP/1.12/24

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

10A	11.28.1		If the payments are not received in accordance with the provisions of Council Decision 482, as amended, on the implementation of cost recovery for notification of satellite network filings, the Bureau shall cancel the publication, after informing the administration concerned. The Bureau shall inform all administrations of such action, and that the network specified in the publication in question no longer has to be taken into consideration by the Bureau and other administrations. The Bureau shall send a reminder to the notifying administration not later than two months prior to the deadline for the payment in accordance with Council Decision 482 unless the payment has already been received. See also Resolution 87 (WRC-03).

Reasons:  New footnote that takes into account Council 05 decision to include notification in satellite network cost recovery requirements.

MOD 		DIAP/ 1.12/25

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

appendix 30 (Rev. WRC-07)*

Article 5   (WRC-07)

Notification, examination and recording in the Master International Frequency Register of frequency assignments to space stations in the 
broadcasting-satellite service

Reasons:  Consequential editorial change.

MOD 		DIAP/1.12/26

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

5.1.6	Upon receipt of a complete notice, the Bureau shall include19A its particulars, with the date of receipt, in its BR IFIC, which shall contain the particulars of all such notices received since the publication of the previous Circular.

Reasons:  Add a footnote to point to new footnote 19A which takes into account satellite network cost recovery for notification.

ADD 		DIAP/1.12/27

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

19A	If the payments are not received in accordance with the provisions of Council Decision 482, as amended, on the implementation of cost recovery for notification of satellite network filings, the Bureau shall cancel the publication, after informing the administration concerned. The Bureau shall inform all administrations of such action, and that the network specified in the publication in question no longer has to be taken into consideration by the Bureau and other administrations. The Bureau shall send a reminder to the notifying administration not later than two months prior to the deadline for the payment in accordance with Council Decision 482 unless the payment has already been received. See also Resolution 87 (WRC-03).

Reasons:  New footnote that takes into account Council 05 decision to include notification in satellite network cost recovery requirements.

MOD 		DIAP/1.12/28

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

APPENDIX 30A (REV. WRC-07)*

Article 5   (WRC-07)

Coordination, notification, examination and recording in the Master

International Frequency Register of frequency assignments to

feeder-link transmitting earth stations and receiving

space stations in the fixed-satellite service21

Reasons:  Consequential editorial change.

MOD 		DIAP/1.12/29

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

    - Upon receipt of a complete notice, the Bureau shall include23A its particulars, with the date of receipt, in its BR IFIC which shall contain the particulars of all such notices received since the publication of the previous Circular.

Reasons:  Add a footnote to point to new footnote 23A which takes into account satellite network cost recovery for notification.

ADD 		DIAP/1.12/30

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

23A	If the payments are not received in accordance with the provisions of Council Decision 482, as amended, on the implementation of cost recovery for notification of satellite network filings, the Bureau shall cancel the publication, after informing the administration concerned. The Bureau shall inform all administrations of such action, and that the network specified in the publication in question no longer has to be taken into consideration by the Bureau and other administrations. The Bureau shall send a reminder to the notifying administration not later than two months prior to the deadline for the payment in accordance with Council Decision 482 unless the payment has already been received. See also Resolution 87 (WRC-03).

Reasons:  A new footnote that takes into account Council 05 decision to include notification in satellite network cost recovery requirements.

MOD 		DIAP/1.12/31

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

appendix 30b (Rev. wrc-07)

Article 8 (WRC-07)

Procedure for notification and recording in the Master Register of assignments in the planned bands for the fixed-satellite service

Reasons:  Consequential editorial change.

MOD 		DIAP/1.12/32

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

  - Complete notices shall be marked by the Bureau with their date of receipt and shall be examined in the date order of their receipt. Following receipt of a complete notice the Bureau shall, within not more than two months, publish3A its contents, with any diagrams and maps and the date of receipt, in the BR IFIC, which shall constitute the acknowledgement to the notifying administration of receipt of its notice. When the Bureau is not in a position to comply with the time-limit referred to above, it shall periodically so inform the administrations, giving the reasons therefore.

Reasons:  Add a footnote to point to new footnote 3A which takes into account satellite network cost recovery requirements for notification.

ADD 		DIAP/1.12/33

Support: Brazil, Canada, Dominican Republic, United States of America, Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama], [Paraguay], [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago],  [Venezuela]

3A	If the payments are not received in accordance with the provisions of Council Decision 482, as amended, on the implementation of cost recovery for notification of satellite network filings, the Bureau shall cancel the publication, after informing the administration concerned. The Bureau shall inform all administrations of  such action, and that the network specified in the publication in question no longer has to be taken into consideration by the Bureau and other administrations. The Bureau shall send a reminder to the notifying administration not later than two months prior to the deadline for the payment in accordance with Council Decision 482 unless the payment has already been received. See also Resolution 87 (WRC-03).

Reasons:  New footnote that takes into account Council 05 decision to include notification in satellite network cost recovery requirements.

It is noted that the date of entry into force of the modifications to the Radio Regulations addressing the consequences of non-payment of satellite network cost recovery fees for notification along with appropriate modifications to Resolution 87 (WRC-03) will also be needed.

Agenda item 2:  To examine the revised ITU-R Recommendations incorporated by reference in the Radio Regulations communicated by the Radio Assembly in accordance with Resolution 28 (Rev. WRC-03),  and to decide whether or not to update the corresponding references in the Radio Regulations, in accordance with the principles contained in Resolution 27 (WRC-03).

Background information

Resolution 28 (Rev. WRC-03) urges Administrations to examine any indicated revisions of ITU-R Recommendations containing text incorporated by reference and to prepare proposals on possible updating of relevant references in the Radio Regulations.

Annex 1 to Resolution 27 (Rev. WRC-03) lists the principles for incorporation by reference.  Principle 5 states:

“If, between WRCs, a text incorporated by reference (e.g. an ITU-Recommendation) is updated, the reference in the Radio Regulations shall continue to apply to the earlier version incorporated by reference until such time as a competent WRC agrees to incorporate the new version.  The mechanism of considering such as step is given in Resolution 28 (Rev. WRC-03).”

Accordingly, proposals are included below to update the references in the Radio Regulations to ITU-R Recommendations incorporated by reference to reflect the latest version, where it is deemed appropriate.

Resolution 27 (Rev. WRC-03) invites Administrations to submit proposals to future conferences, taking into account the CPM Report, in order to clarify the status of references, where ambiguities remain regarding the mandatory or non-mandatory status of the references in question, with a view to amending those references:

- that appear to be of a mandatory nature, identifying such references as being incorporated by reference by using clear linking language in accordance to Annex 2;

- that are of a non-mandatory character, so as to refer to “the most recent version” of the Recommendations.

Accordingly, proposals are included below to clarify the status of existing references to ITU-R Recommendations and to correct, among other things, any remaining ambiguities.

The CPM Report addresses the two types of proposals described above (i.e. 1. updating references in the RR to reflect new versions of ITU-R Recommendations and 2. clarifying the status of references) and was used as the basis for some of the proposals included below.  The CPM Report also  describes a third situation where a WRC Resolution includes a resolves referring to an ITU-R Recommendation using mandatory language (i.e., shall).  In this situation, the ITU-R Recommendation or parts thereof, as may be specified, are considered to be incorporated by reference.  Therefore, in order to clarify the scope of incorporation by reference and confirm the treatment of those ITU-R Recommendations, Resolution 27 (Rev.WRC-03) should be modified accordingly.

Regarding the incorporation by reference of Recommendation ITU-R M.1642-1 into the Radio Regulations, both this latter situation of incorporation by reference via a WRC Resolution and the need to update the reference in the RR apply.  It is noted that consequential changes to the Radio Regulations in relation to this proposal may be addressed under Agenda item 3.

## Proposal for Agenda item 2:  Recommendation ITU-R M.541

VOLUME 4

ITU-R Recommendations incorporated by reference

MOD 	DIAP/ 2/

Support: [Brazil], [Canada], Dominican Republic, United States of America, Paraguay, [Suriname], Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis],  [Trinidad and Tobago],  [Venezuela]

RECOMMENDATION  ITU-R  M.541-9*

OPERATIONAL  PROCEDURES  FOR  THE  USE  OF  DIGITAL  SELECTIVE-CALLING
EQUIPMENT  IN  THE  MARITIME  MOBILE  SERVICE

(Question ITU-R 9/8)

(1978-1982-1986-1990-1992-1994-1995-1996-1997)

Reasons:  This Recommendation was updated to Rev. 9 on 5/2004.  The updated revision was examined as requested by Resolution 28 (Rev. WRC-03).  It is appropriate to update the corresponding reference in the Radio Regulations, in accordance with the principles contained in the Annex to Resolution 27 (Rev. WRC-03).

## Proposal for Agenda item 2:  Recommendation ITU-R P.833

MOD 	DIAP/ 2 /

Support: [Brazil], [Canada], Dominican Republic, United States of America, Paraguay, [Suriname], Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis],  [Trinidad and Tobago],  [Venezuela]

RECOMMENDATION  ITU-R  P.838-3

Specific attenuation model for rain for use in prediction methods

(Question ITU-R 201/3)

(1992-1999-2003)

Reasons:  This Recommendation was updated to Rev. 3 on 5/2004.  The updated revision was examined as requested by Resolution 28 (Rev. WRC-03).  It is appropriate to update the corresponding reference in the Radio Regulations, in accordance with the principles contained in the Annex to Resolution 27 (Rev. WRC-03).

## Proposal for Agenda item 2:  Recommendation ITU-R M.1174

MOD 	DIAP/ 2/

Support: [Brazil], [Canada], Dominican Republic, United States of America, Paraguay, [Suriname], Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis],  [Trinidad and Tobago],  [Venezuela]

RECOMMENDATION  ITU-R  M.1174-2*

TECHNICAL  CHARACTERISTICS  OF  EQUIPMENT  USED
FOR  ON-BOARD  VESSEL  COMMUNICATIONS  IN
THE  BANDS  BETWEEN  450  AND  470  MHz

(1995-1998)

Reasons:  This Recommendation was updated to Rev. 2 on 5/2004.  The updated revision was examined as requested by Resolution 28 (Rev. WRC-03).  It is appropriate to update the corresponding reference in the Radio Regulations, in accordance with the principles contained in the Annex to Resolution 27 (Rev. WRC-03).

## Proposal for Agenda item 2:  Recommendation ITU-R M.1642

ADD 	DIAP/ 2/

Support: [Brazil], [Canada], Dominican Republic, United States of America, Paraguay, [Suriname], Uruguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia],   [Chile], [Colombia], [Costa Rica], [Dominica],  [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis],  [Trinidad and Tobago],  [Venezuela]

RECOMMENDATION  ITU-R  M.1642-1

Methodology for assessing the maximum aggregate epfd at an aeronautical radionavigation service station from all radionavigation-satellite service systems operating in the 1 164-1 215 MHz band

(2007)

Reasons:	Footnote 5.328A (WRC-03) states that RNSS systems operating in the band 1164-1215 MHz shall operate in accordance with the provisions of Resolution 609 (WRC-03).  Resolves 10 of this Resolution states that Recommendation ITU-R M. 1642 shall be used to perform the requisite calculations related to this resolution.  Therefore, the revised referenced Recommendation fulfills the criteria to be incorporated into the Radio Regulations.

The previous Agenda item 2 proposals may require consequential changes to the Radio Regulations, in accordance with Agenda item 3.

## Proposals for Agenda item 2:  References to ITU-R Recommendations in the Radio Regulations requiring modification to bring them into accordance with Resolution 27 (Rev.WRC-03) (Annex 2, No. 5)

It is proposed to modify the footnotes and provisions as shown in Section 7/2/1 of the CPM Report.  With respect to 5.536A, Option 1 is supported. Please below the text.

Incorporation by reference of ITU-R Recommendations mentioned in Volumes 1 and 2 of the Radio Regulations – Changes to provisions of a non-mandatory nature

It was noted that references to ITU-R Recommendations of non-mandatory character do not need to be updated by a WRC.

It was noted that Resolutions 27 (Rev.WRC-03) and 28 (Rev.WRC-03) do not contain a procedure for updating the references to ITU-R Recommendations of non-mandatory character.

WRC-07 may wish to consider the need to establish such a procedure and to adopt the necessary texts as appropriate.

The various footnotes and provisions in the RR were examined by the Special Committee, from the point of view of incorporation by reference and were submitted to the CPM. The CPM preferred not to study them and are sent to WRC-07 for information.

MOD		DIAP/2/5

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

5.208A		In making assignments to space stations in the mobile-satellite service in the bands 137-138 MHz, 387-390 MHz and 400.15-401 MHz, administrations shall take all practicable steps to protect the radio astronomy service in the bands 150.05-153 MHz, 322-328.6 MHz, 406.1-410 MHz and 608-614 MHz from harmful interference from unwanted emissions. The threshold levels of interference detrimental to the radio astronomy service are shown in Table 1 of Recommendation ITU-R RA.769.     (WRC-07)

Reasons:	To conform to Resolution 27 (Rev.WRC-03) (Annex 2, § 5), as the language indicates this Recommendation is not mandatory and it is not in RR Volume 4.

Regarding No. 5.536A, two options were identified:

Option 1:

MOD 	DIAP/2/6

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

5.536A		Administrations operating earth stations in the Earth exploration-satellite service or the space research service shall not claim protection from stations in the fixed and mobile services operated by other administrations. In addition, earth stations in the Earth exploration-satellite service or in the space research service should be operated taking into account the most recent versions of Recommendations ITU-R SA.1278 and ITU-R SA.1625, respectively.     (WRC-07)

Reasons:	To conform to Resolution 27 (Rev.WRC-03) (Annex 2, § 5), as the “should” language indicates this Recommendation is not mandatory and is not in RR Volume 4.

MOD 		DIAP/2/7

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

16.2	The international monitoring system comprises only those monitoring stations so nominated by administrations in the information sent to the Secretary-General which should be in accordance with the most recent version of Recommendation ITU-R SM.1139. These stations may be operated by an administration or, in accordance with an authorization granted by the appropriate administration, by a public or private enterprise, by a common monitoring service established by two or more countries, or by an international organization.  (WRC-07)

MOD 		DIAP/2/8

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

  - Administrative and procedural requirements for use and operation of the international monitoring system should be in accordance with the provisions of the most recent version of Recommendation ITU-R SM.1139.  (WRC-07)

MOD 		DIAP/2/9

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

22.36		Earth stations operating in the frequency band 29.5-30 GHz should be designed in such a manner that 90% of their peak off-axis e.i.r.p. density levels do not exceed the values given in No. 22.32. Further study is needed to determine the off-axis angular range over which these exceedences would be permitted, taking into account the interference level into adjacent satellites. The statistical processing of the off-axis e.i.r.p. density peaks should be carried out using the method given in the most recent version of Recommendation ITU-R S.732.   (WRC-07)

MOD 		DIAP/2/10

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

51.71	§ 28	In the case of communication between stations on board aircraft and stations of the maritime mobile service, radiotelephone calling may be renewed as specified in the most recent version of Recommendation ITU-R M.1171 and radiotelegraph calling may be renewed after an interval of five minutes, notwithstanding the procedure contained in the most recent version of Recommendation ITU-R M.1170.  (WRC-07)

MOD 		DIAP/2/11

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

56.2	§ 2	The procedures specified in  the most recent version of Recommendation ITU-R M.492 should be employed except in cases of distress, urgency, or safety, in which case alternate or non-standard procedures may be used.   (WRC-07)]

MOD 		DIAP/2/12

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

APPENDIX 4 (Rev.WRC-07)

Consolidated list and tables of characteristics for use in the

application of the procedures of Chapter III

ANNEX 2

Characteristics of satellite networks, earth stations

or radio astronomy stations2 (WRC-07)

Information relating to the data listed in the following Tables

In many cases the data requirements involve the use of standard symbols in submissions to the Radiocommunication Bureau. These standard symbols may be found in the “Preface to the BR International Frequency Information Circular”, (BR IFIC) (Space Services) and the Space Radiocommunication Stations on CD-ROM. (In the Table, this is referred to simply as “the Preface”.) Information relating to the provision of data may also be found in ITU-R Recommendations, for example, information on the mask data can be found in the most recent version of Recommendation ITU-R S.1503 and the most recent version of Recommendation ITU-R SM.1413 provides general information related to submission of data.

MOD 		DIAP/2/13

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

APPENDIX 5 (Rev.WRC-07)

Identification of administrations with which coordination is to be effected or

agreement sought under the provisions of Article 9

ANNEX 1 (WRC-07)

1	Coordination thresholds for sharing between MSS (space-to-Earth) and  terrestrial  services  in  the  same  frequency  bands  and  between non-GSO MSS feeder links (space-to-Earth) and terrestrial services in the same frequency bands

1.2.1	Objectives

As a consequence of this new concept, the need for coordination between space stations of the MSS (space-to-Earth) and terrestrial services is determined using two methods:

- 	simple method: FDP (simple definition of the MSS system and characteristics of reference FS stations are used in inputs) or power flux-density trigger value;

-	more detailed method: system specific methodology (SSM) (specific characteristics of the

MSS system and characteristics of reference fixed service stations are used in inputs) as described, for example, in the most recent version of Annex 1 to Recommendation ITU-R M.1143.

1.2.3.2	A system specific methodology (SSM) to be used in determining the need for detailed coordination of non-GSO MSS (space-to-Earth) systems with fixed service systems

Those administrations planning to establish the need for coordination between non-GSO MSS networks and fixed service systems are encouraged to use the most recent version of Recommendation ITU-R M.1143. While urgent additional development work is being undertaken in the ITU-R to facilitate the use of the methodology described in the most recent version of Recommendation ITU-R M.1143, administrations may be able to effect coordination by applying this SSM.

Reasons:  Use of these ITU-R Recommendations are considered not mandatory in nature and to correct the ambiguity and clarify the linking language to conform to Resolution 27 (Rev. WRC-03) (Annex 2, No. 5).

## Proposals for Agenda item 2:  Incorporation by reference of ITU-R Recommendations mentioned in WRC Resolutions

DIAP/2/14

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

It is proposed to modify Annex 1 to Resolution 27 (Rev.WRC-03) as shown in Section 7/2/2 of the CPM Report.

Reasons:	In order to better clarify the scope of incorporation by reference and confirm the treatment of ITU-R Recommendations pursuant to Resolution 27 (Rev.WRC-03).

DIAP/2/15

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

It is proposed to add the ITU-R Recommendations listed in Table 1 of Section 7/2/2 to Volume 4 of the Radio Regulations.   It should be noted that there are revised versions for some of these ITU-R Recommendations, i.e., ITU-R S.1428-1, ITU-R BO.1443-2 and M.1642-1, and it is these versions that should be included in Volume 4.

Reasons:	Use of the term “shall” in the resolves is mandatory in nature and consequently incorporates by reference the specified ITU-R Recommendation, or parts thereof.

## Proposals for Agenda item 2:  ITU-R Recommendations incorporated by reference in the Radio Regulations which have been revised and approved since WRC-03

Section 7/2/3 of the CPM Report identifies ITU-R Recommendations which have been revised and approved during the elapsed study period since WRC-03.  The following provisions require the corresponding references be updated to reflect the revised and approved version of the concerned ITU-R Recommendation.

MOD 		DIAP/2/16

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

5.279A	The use of this band by sensors in the Earth exploration-satellite service (active) shall be in accordance with Recommendation ITU-R RS.1260-1. Additionally, the Earth exploration-satellite service (active) in the band 432-438 MHz shall not cause harmful interference to the aeronautical radionavigation service in China. The provisions of this footnote in no way diminish the obligation of the Earth  exploration-satellite service (active) to operate as a secondary service in accordance with Nos. 5.29 and 5.30. (WRC-07)

[Editor’s note:  Recommendation ITU-R SA.1260-1 was renamed to the RS series.]

MOD 		DIAP/2/17

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

5.287	In the maritime mobile service, the frequencies 457.525 MHz, 457.550 MHz, 457.575 MHz, 467.525 MHz, 467.550 MHz and 467.575 MHz may be used by on-board communication stations. Where needed, equipment designed for 12.5 kHz channel spacing using also the additional frequencies 457.5375 MHz, 457.5625 MHz, 467.5375 MHz and 467.5625 MHz may be introduced for on-board communications. The use of these frequencies in territorial waters may be subject to the national regulations of the administration concerned. The characteristics of the equipment used shall conform to those specified in Recommendation ITU-R M.1174-2*.   (WRC-07)

MOD 		DIAP/2/18

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

5.288		In the territorial waters of the United States and the Philippines, the preferred frequencies for use by on-board communication stations shall be 457.525 MHz, 457.550 MHz, 457.575 MHz and 457.600 MHz paired, respectively, with 467.750 MHz, 467.775 MHz, 467.800 MHz and 467.825 MHz. The characteristics of the equipment used shall conform to those specified in Recommendation ITU-R M.1174-2.   (WRC-07)

MOD 		DIAP/2/19

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

5.447F	In the band 5 250-5 350 MHz, stations in the mobile service shall not claim protection from the radiolocation service, the Earth exploration-satellite service (active) and the space research service (active). These services shall not impose on the mobile service more stringent protection criteria, based on system characteristics and interference criteria, than those stated in Recommendations ITU-R M.1638 and ITU-R RS.1632.   (WRC-07)

[Editor’s note:  Recommendation ITU-R SA.1632 was renamed to the RS series.]

MOD 		DIAP/2/20

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

1222.5C.11	For this Table, reference patterns of Annex 1 to Recommendation ITU-R BO.1443-2 shall be used only for the calculation of interference from non-geostationary-satellite systems in the fixed-satellite service into geostationary-satellite systems in the broadcasting-satellite service.   (WRC-07)

MOD 		DIAP/2/21

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

51.35	b)	send and receive class F1B or J2B emissions on an international calling channel (identified in Recommendation ITU-R M.541-9) in each of the HF maritime mobile bands necessary for their service;   (WRC-07)

MOD 		DIAP/2/22

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

52.148		b)	 subject to the provisions of No. 52.149, one of the international digital selective-calling frequencies indicated in Recommendation ITU-R M.541-9.   (WRC-07)

MOD 		DIAP/2/23

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

52.149	2)	The international digital selective-calling frequencies indicated in Recommendation ITU-R M.541-9 may be used by any ship station. In order to reduce interference on these frequencies, they shall only be used when calling cannot be made on nationally assigned frequencies.  (WRC-07)

MOD 		DIAP/2/24

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

52.152		b)	subject to the provisions of No. 52.153, one of the international digital selective-calling frequencies indicated in Recommendation ITU-R M.541-9.  (WRC-07)

MOD 		DIAP/2/25

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

52.153	2)	The international digital selective-calling frequencies indicated in Recommendation ITU-R M.541-9 may be assigned to any coast station. In order to reduce interference on these frequencies, they may be used as a general rule by coast stations to call ships of another nationality, or in cases where it is not known on which digital selective-calling frequencies within the bands concerned the ship station is maintaining watch.   (WRC-07)

MOD 		DIAP/2/26

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

52.159	§ 71	1) The frequency 156.525 MHz is an international frequency in the maritime mobile service used for distress, urgency, safety and calling by digital selective-calling techniques (see Nos. 33.8 and 33.31, Appendix 15 and Recommendation ITU-R M.541-9). (WRC-07)

MOD 		DIAP/2/27

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

54.2			2)	Selective calling may be carried out using a sequential single-frequency code system which shall be in accordance with Recommendation ITU-R M.257-3 or a digital selective-calling system which shall be in accordance with Recommendations ITU-R M.493-11, ITU-R M.541-9, ITU-R M.821-1 and ITU-R M.825-3 in the shore-to-ship, ship-to-shore and ship-to-ship directions.   (WRC-07)

MOD 		DIAP/2/28

Support: Canada, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador], [United States of America], [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

APPENDIX 4 (Rev.WRC-07)

Consolidated list and tables of characteristics for use in the

application of the procedures of Chapter III

ANNEX 2 (WRC-07)

Characteristics of satellite networks, earth stations

or radio astronomy stations2 (WRC-07)

Table C

Items in Appendix

C.11.b

the appropriate information required to calculate the affected region (as defined in Recommendation ITU-R M.1187-1)

Required only for a non-geostationary space station in the mobile-satellite service submitted in Accordance with No. 9.11A

Reasons:	These ITU-R Recommendations have been revised since the last conference or since the last publication of the Radio Regulations.  The corresponding provisions are modified in accordance with Resolution 28 (Rev.WRC-03).   With respect to 5.279A and 5.447F, Recommendations ITU-R SA.1260-1 and SA.1632 were renamed in the RS series.  Also, Recommendations ITU-R M.493-9, M.821-1 and M.825-2 are currently not included in Volume 4 of the Radio Regulations and consequently should be placed therein, however with the most recent version.

# ______

Agenda item 4

In accordance with Resolution 95 (Rev.WRC-2003), to review the Resolutions and Recommendations of the previous Conferences with a view to their possible revision, replacement or abrogation.

Background information

Resolution 33 (Rev. WRC-03) contains procedures to be applied for the coordination and notification of BSS satellite networks for which the API has been received by the Radiocommunications Bureau prior to 1 January 1999.

The BR Director's review of Resolutions and Recommendations of WARC/WRC, submitted to the last meeting of the CPM, proposed that WRC-07 suppress Resolution 33 (Rev.WRC-03) under the justification "Processing of filings under this Resolution completed".

However, some countries still have BSS filings in the process of coordination and notification in accordance with the terms of Resolution 33 (Rev. WRC-03). These filings have been submitted under 11.43A and are covered by an API submitted prior to 1 January 1999. Moreover, their validity extends well beyond 2007.

## Proposal for Agenda item 4:  Resolution 33 (Rev. WRC-03)

NOC 		DIAP/4/1

Support: Canada, United States of America, Paraguay

[Antigua and Barbuda], [Argentina], [Bahamas], [Barbados], [Belize], [Bolivia], [Brazil],  [Chile], [Colombia], [Costa Rica], [Dominica], [Dominican Republic], [Ecuador], [El Salvador],  [Grenada], [Guatemala], [Guyana], [Haiti], [Honduras], [Jamaica], [Mexico], [Nicaragua], [Panama],  [Peru], [Saint Lucia], [Saint Vincent and the Grenadines], [Saint Kitts and Nevis], [Suriname], [Trinidad and Tobago], [Uruguay], [Venezuela]

RESOLUTION 33 (Rev.WRC-03)

Bringing into use of space stations in the broadcasting-satellite service,

prior to the entry into force of agreements and associated plans for

the broadcasting-satellite service

Reasons:   Suppression of Resolution 33 (Rev. WRC-03) by WRC-07 is not appropriate because it will modify in mid-course the coordination and notification procedures applicable to certain filings still in process within the ITU.

# ______

# Footnotes

*	This Recommendation should be brought to the attention of the International Maritime Organization (IMO) and the ITU Telecommunication Standardization Sector (ITU-T).

* 	This Recommendation should be brought to the attention of the International Maritime Organization (IMO) and the International Maritime Radio Committee (CIRM).

* Note of the Secretariat: Resolution 341 was abrogated by WRC-03