| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 3 to Document 5-E |
|  | 7 September 2007 |
|  | Original: English |
| United States of America |
| proposals for the work of the conference |
| Agenda item 1.12 |

1.12	to consider possible changes in response to Resolution 86 (Rev. Marrakesh, 2002) of the Plenipotentiary Conference: “Advance publication, coordination, notification and recording procedures for frequency assignments pertaining to satellite networks” in accordance with Resolution 86 (WRC-03)

Provisions of RR No. 22.2

Background information

RR No. 22.2 is the provision that governs the sharing between non-geostationary satellite (non-GSO) systems vis-à-vis geostationary satellite (GSO) networks in the fixed-satellite service (FSS) and the broadcasting-satellite service (BSS), except when it is explicitly disabled through a footnote in RR Article 5 or through a Resolution adopted by a World Radiocommunication Conference (WRC).

Section 6/1.12/5 of the CPM Report specifies that there are two and only two situations in the RRs with regard to No. 22.2. In the first case, No. 22.2 has been removed from a particular FSS or BSS band, putting non-GSO systems on an equal footing with BSS or FSS GSO networks (as the case may be). In the second case, No. 22.2 is quantified (e.g. No. 22.5I by meeting the epfd limits) and the provisions of Article 5 contain footnotes that preclude a non-GSO system from claiming protection from a GSO FSS/BSS network that is operating in accordance with the Radio Regulations (e.g. No. 5.484A).

In a frequency band where No. 22.2 has been disabled, the language of No. 22.2, current or modified, is irrelevant. In the second case above, copying Article 5 text that obligates non-GSO systems not to claim protection from a GSO into No. 22.2 appears not to do anything that the RRs do not already do. In both of these cases, then, there is no reason to change No. 22.2 in the manner suggested in the CPM Report.

The CPM Report fails to mention that there are additional cases of how No. 22.2 is applied that are not covered by Section 6/1.12/5. One omitted case involves the numerous FSS and unplanned BSS bands where No. 22.2 remains applicable, but where no EPFD limits have been adopted and No. 9.11A is not applied. An example of these bands is the pair of FSS bands at 37.5-42.5 GHz and 47.2-50.2 GHz. In these bands, WRC-03 has held open the possibility that greater flexibility and

sharing between non-GSO and GSO FSS systems may emerge. It specified, in considering g) and h) of Resolution 136 (Rev.WRC-03):

“g)	that in the frequency range 37.5-50.2 GHz where there has been little or no deployment of satellite systems to date, administrations concerned with both GSO FSS and non-GSO FSS systems should be expected to exhibit flexibility in achieving the appropriate balance in the sharing environment;

h)	that this Conference, having considered the outcome of the ITU-R studies on this subject, as summarized in the CPM Report to this Conference, has decided that further studies are needed before the conditions for non-GSO FSS systems to share these bands with GSO FSS networks can reliably be determined,”.

Changing No. 22.2, which applies in the Resolution 136 bands, in the manner suggested in the CPM Report example, would prejudge these important studies, and possibly remove flexibility that WRC-03 wanted to preserve.

No. 22.2 of the Radio Regulations was modified at WRC-97, and appears to have worked very well since then. The current regulation was the basis of EPFD limitations adopted at WRC-2000 and WRC-03 in a number of FSS and BSS frequency bands.

The only justification given in the CPM Report for changing the provision is that the new words would duplicate material already in Article 5 footnotes. This is not universally so in bands where No. 22.2 applies, as noted above. Even if it were so, it is questionable at best whether adding language to No. 22.2 that is already in the RRs is a suitable justification for changing No. 22.2. The regulations are not inconsistent today.

Finally, it simply does not make sense to revisit one of the most controversial and heavily debated regulations of recent WRCs without having very good cause to do so. No. 22.2 is the basis for a number of limits on non-GSO satellite systems. There are associated provisions in some bands that apply to GSO networks to provide some protection to non-GSO systems. Changing the language of No. 22.2 in the manner suggested in the CPM Report may unintentionally disturb this delicate balance, and necessitate revisiting matters that are now successfully resolved.

For all of these reasons, the proposal below is that the text of No. 22.2 of the Radio Regulations NOT be changed in any way by WRC-07.

ARTICLE  22

Space services1

Section II  –  Control of interference to geostationary-satellite systems

NOC	USA/5A3/1

22.2	§ 2	1)	Non-geostationary-satellite systems shall not cause unacceptable interference to geostationary-satellite systems in the fixed-satellite service and the broadcasting-satellite service operating in accordance with these Regulations.     (WRC-97)

Reasons:	The reasons provided in the CPM Report are incomplete; other cases exist where changing No. 22.2 as shown in the CPM Report would prejudice the sharing situation. Modifying such an important and historically controversial regulation as No. 22.2 could disturb a delicate balance that is reflected in many RRs, and could have unintended negative consequences.

Modification of Appendix 5 (equal rights ONLY)

Background information

Appendix 5 (Rev.WRC-03) – Identification of administrations with which coordination is to be effected or agreement sought under the provisions of Article 9, paragraph 1 reads as follows:

“1	For the purpose of effecting coordination under Article 9, except in the case under No. 9.21, and for identifying the administrations with which coordination is to be effected, the frequency assignments to be taken into account are those in the same frequency band as the planned assignment, pertaining to the same service or to another service to which the band is allocated with equal rights or a higher category1 of allocation, which might affect or be affected, as appropriate, and which are: ...”

The purpose of this proposal is to consider the phrase, “to which the band is allocated with equal rights or a higher category”. The Radio Regulations are very clear that in some situations coordination is limited to services with equal rights:

1)	No. 9.15 states, “… in respect of terrestrial stations in frequency bands allocated with equal rights to space and terrestrial services ...”

2)	No. 9.17 states, “… allocated with equal rights to space and terrestrial services, ...”

3)	No. 9.17A states, “... in frequency bands allocated with equal rights to space radiocommunication services in both directions of transmission …”

No. 9.11A applies “the provisions of Nos. 9.12 to 9.16” and the Rule of Procedure (RoP) on No. 9.11A specifies that the procedure of No. 9.11A is applicable to, “... satellite services having allocations with equal rights …”. Additionally, while there is no text in the RR or in the RoP on No. 9.7 it doesn’t appear that administrations responsible for geostationary-satellite networks should have to coordinate if they are not allocated on an equal basis. Based on the current principle of “allocated with equal rights or a higher category of allocation,” new GSO networks allocated on a secondary basis have to coordinate under this provision with the GSO networks allocated on a primary basis that are ahead of them, but not with the GSO networks behind them in the process.

Also, the successful coordination between stations with primary and secondary allocations may infer, or lead to confusion, of the status of the rights of the station with a secondary allocation.

While it may appear that coordination between primary and secondary services may provide for an opportunity for them to agree on ways the secondary service can operate compatibly with the primary service, it is recognized that there is no incentive for a secondary service to coordinate with a primary service, as no reciprocity is allowed and the provisions of Nos. 5.28 to 5.31 apply regardless of the result of the coordination procedure. Any such discussions could take place on a bilateral basis between the administrations, including during the Advance Publication process or when the secondary GSO network coordination special section is published for coordination with other networks allocated on a secondary basis.

APPENDIX  5  (Rev.WRC-03)

Identification of administrations with which coordination is to be effected or 
agreement sought under the provisions of Article 9

MOD	USA/5A3/2

1	For the purpose of effecting coordination under Article 9, except in the case under No. 9.21, and for identifying the administrations with which coordination is to be effected, the frequency assignments to be taken into account are those in the same frequency band as the planned assignment, pertaining to the same service or to another service to which the band is allocated with equal rights, which might affect or be affected, as appropriate, and which are:

Reasons:	To clarify that Nos. 9.7 and 9.11A to 9.19 apply only between assignments in bands allocated with equal rights.

_____________

# Footnotes

1	The coordination between an earth station and terrestrial stations under Nos. 9.15, 9.16, 9.17, 9.18 and 9.19, or between earth stations operating in opposite directions of transmission under 9.17A, applies only to assignments in bands allocated with equal rights.