| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 4 to Document 5-E |
|  | 7 September 2007 |
|  | Original: English |
| United States of America |
| proposals for the work of the conference |
| Agenda item 1.20 |

1.20	to consider the results of studies, and proposals for regulatory measures if appropriate regarding the protection of the EESS (passive) from unwanted emissions of active services in accordance with Resolution 738 (WRC-03)

Background information

The resolves in Resolution 738 (WRC-03) call for three actions: 1) studying the compatibility between EESS (passive) and the corresponding active services listed in the Table in Resolution 738 to update Recommendation ITU-R SM.1633 or develop additional Recommendations; 2) further studying the impact of implementing the values in considering f) and g)1 in the bands 31-31.3 GHz and 51.4-52.6 GHz for unwanted emissions of systems operating in Regions 2 and 3, taking into account that the impact on fixed-service systems in Region 1 is documented in Recommendation ITU-R SM.1633; and 3) reviewing the results of studies in 1) and 2) in order to consider regulatory measures, if appropriate, to ensure the protection of the EESS (passive) operating in the bands listed in the table in Resolution 738 (WRC-03) from unwanted emissions of active services operating in the corresponding bands, while taking into account the impact on all concerned services of implementing or not implementing such measures. The table below shows the frequency band and radiocommunication service combinations within the scope of the agenda item.

Studies now documented in Report ITU-R SM.2092 show that active services in some of these bands do not produce significant unwanted emissions in the adjacent passive band. However, active services in other bands may produce unwanted emissions in excess of EESS (passive) protection requirements. For some active service allocations, unwanted emission limits may be practical, while for others, they are clearly not practical. Because of the differences between the active services, and the differences in the use of the active and passive services from band to band, the solutions for this agenda item have been determined on a band-by-band and service-by-service basis.

This proposal provides either new footnotes or “no change,” as appropriate, for active service allocations adjacent to or nearby the EESS (passive) bands. A new Resolution, replacing Resolution 738 (WRC-03), addresses fixed and fixed-satellite service bands above 31 GHz, for which limited information was available for the studies leading up to WRC-07. The new Resolution would encourage future conferences to give adequate consideration to the impact on the EESS (passive) and active services when allocating them to adjacent or nearby frequency bands, recognize the results of studies on the protection of the EESS (passive), call for further conference consideration of these studies and encourage design of active service systems in accordance with the results of studies until a conference can resolve the issue. The proposal does not require, and no provision is made for, Radiocommunication Bureau examination, or enforcement of any limits.

| EESS (passive) band | Active service band | Active service |
| --- | --- | --- |
| 1 400-1 427 MHz | 1 350-1 400 MHz | Fixed service (FS) Mobile service (MS) Radiolocation service (RLS) |
|  | 1 427-1 429 MHz | FS, MS (except aeronautical mobile service (AMS)) and space operation service (Earth-to-space)1 |
|  | 1 429-1 452 MHz | FS and MS |
| 23.6-24 GHz | 22.55-23.55 GHz | Inter-satellite service (ISS) |
| 31.3-31.5 GHz | 30-31 GHz | FSS (Earth-to-space) |
|  | 31-31.3 GHz | FS (except HAPS) |
| 50.2-50.4 GHz2 | 50.4-51.4 GHz2 | FSS (Earth-to-space)2 |
|  | 47.2-50.2 GHz (Regions 2 and 3) 49.44-50.2 GHz2 (Region 1) | FSS2 |
| 52.6-54.25 GHz | 51.4-52.6 GHz | FS |
| 1 Resolution 738 (WRC 03) incorrectly refers to the space research service instead of the space operation service. 2 Studies in this band must take into account No. 5.340.1. |

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	USA/5A4/1

1 300-1 525 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 1 350-1 400 FIXED ADD 5.AAA MOBILE RADIOLOCATION | 1 350-1 400 RADIOLOCATION |
| 5.149 5.338 5.339 5.339A | 5.149 5.334 5.339 5.339A |
| 1 400-1 427 EARTH EXPLORATION-SATELLITE (passive) RADIO ASTRONOMY SPACE RESEARCH (passive) 5.340 5.341 |
| 1 427-1 429 SPACE OPERATION (Earth-to-space) ADD 5.BBB FIXED ADD 5.AAA MOBILE except aeronautical mobile 5.341 |
| 1 429-1 452 FIXED ADD 5.AAA MOBILE except aeronautical mobile | 1 429-1 452 FIXED ADD 5.AAA MOBILE 5.343 |
| 5.339A 5.341 5.342 | 5.339A 5.341 |

ADD	USA/5A4/2

5.AAA	Administrations should take all practicable measures to protect the EESS (passive) when designing and implementing systems and networks in the bands 1 350-1 400 MHz and 1 427-1 452 MHz. The unwanted emissions power in the band 1 400-1 427 MHz delivered to the antenna of any station in the fixed service operating in the band 1 350-1 400 MHz or in the band 1 427-1 452 MHz, should not exceed –45 dBW.

Reasons:	To facilitate the protection of the EESS (passive).

NOC	USA/5A4/3

No change to the Radio Regulations regarding the radiolocation service allocation in the band 1 350-1 400 MHz.

Reasons:	Although studies documented in Report ITU-R SM.2092 show that the radiolocation unwanted emissions in the EESS (passive) band at 1 400-1 427 MHz would exceed the permissible interference threshold in Recommendation ITU-R SA.1029-2, any interference would occur for only short time periods and would be readily discernible by users of the remote sensing data, allowing corrupted data to be discarded. The remaining uncorrupted data is expected to satisfy the scientific objectives of the EESS missions. Studies also show that radars would experience unacceptable degradation in operational coverage and range, target resolution, and accuracy if required to meet unwanted emission limits in the 1 400-1 427 MHz band. As with other pairs of active and passive bands, use of portions of the allocated bands must not be restricted. Radars would suffer an increased likelihood of interference from other radars and a reduction in coverage range, while a reduced bandwidth would be inadequate for remote sensing requirements.

ADD	USA/5A4/4

5.BBB	Administrations should take all practicable measures to protect the EESS (passive) when designing and implementing systems and networks in the band 1 427-1 429 MHz. The unwanted emissions power in the band 1 400-1 427 MHz delivered to the antenna of any earth station in the space operation service (Earth-to-space) operating in the band 1 427-1 429 MHz should not exceed –36 dBW.

Reasons:	To facilitate the protection of the EESS (passive).

NOC	USA/5A4/5

22-24.75 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 22.55-23.55 FIXED INTER-SATELLITE MOBILE 5.149 |
| 23.55-23.6 FIXED MOBILE |
| 23.6-24 EARTH EXPLORATION-SATELLITE (passive) RADIO ASTRONOMY SPACE RESEARCH (passive) 5.340 |

NOC	USA/5A4/6

No change to the Radio Regulations regarding the inter-satellite service allocation in the band 22.55-23.55 GHz.

Reasons:	Results of studies documented in Report ITU-R SM.2092 show that unwanted emissions from the ISS in the 22.55-23.55 GHz band are well below the recommended protection criteria for the EESS (passive) in the 23.6-24.0 GHz band. Therefore, no changes are needed to the Radio Regulations to protect the EESS (passive) in the 23.6-24.0 GHz band from unwanted emissions from the ISS in the 22.55-23.55 GHz band.

MOD	USA/5A4/7

29.9-34.2 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 30-31 FIXED-SATELLITE (Earth-to-space) MOBILE-SATELLITE (Earth-to-space) Standard frequency and time signal-satellite (space-to-Earth) 5.542 |
| 31-31.3 FIXED 5.543A ADD 5.CCC MOBILE Standard frequency and time signal-satellite (space-to-Earth) Space research 5.544 5.545 5.149 |
| 31.3-31.5 EARTH EXPLORATION-SATELLITE (passive) RADIO ASTRONOMY SPACE RESEARCH (passive) 5.340 |

NOC	USA/5A4/8

No change to the Radio Regulations regarding the fixed-satellite service (Earth-to-space) allocation in the band 30-31 GHz.

Reasons:	Results of studies documented in Report ITU-R SM.2092 show that unwanted emissions from the FSS in the 30-31 GHz band do not exceed the recommended protection criteria for the EESS (passive) in the 31.3-31.5 GHz band. The FSS allocation is separated from the EESS (passive) allocation by 300 MHz, which greatly reduces the possibility of FSS unwanted emissions exceeding the protection criteria in the EESS (passive) band. Unwanted emission limits in the EESS (passive) band are unnecessary, and could constrain the future development of FSS uplink transmitters in the 30-31 GHz band.

ADD	USA/5A4/9

5.CCC	In the bands:

31-31.3 GHz,
47.2-50.2 GHz,
50.4-51.4 GHz,
51.4-52.6 GHz,

Resolution [AI 1.20] (WRC-07) applies.

Reasons:	Studies documented in Report ITU-R SM.2092 indicate that unwanted emissions from fixed service transmitters in the bands 31-31.3 GHz and 51.4-52.6 GHz, and from fixed-satellite service (Earth-to-space) earth stations in the bands 47.2-50.2 GHz and 50.4-51.4 GHz, may cause unacceptable interference to the Earth exploration-satellite (passive) service in the adjacent bands 31.3-31.5 GHz, 50.2-50.4 GHz and 52.6-54.25 GHz. The fixed service in the bands 31-31.3 GHz and 51.4-52.6 GHz, and the fixed-satellite service (Earth-to-space) in the bands 47.2-50.2 GHz and 50.4-51.4 GHz, are in the early stages of development.

MOD	USA/5A4/10

40-47.5 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 47.2-47.5 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.CCC MOBILE 5.552A |

MOD	USA/5A4/11

47.5-51.4 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 47.5-47.9 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.CCC (space-to-Earth) 5.516B 5.554A MOBILE | 47.5-47.9 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.CCC MOBILE |
| 47.9-48.2 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.CCC MOBILE 5.552A |
| 48.2-48.54 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.CCC (space-to-Earth) 5.516B 5.554A 5.555B MOBILE | 48.2-50.2 FIXED FIXED-SATELLITE (Earth-to-space) 5.516B 5.552 ADD 5.CCC MOBILE |
| 48.54-49.44 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.CCC MOBILE 5.149 5.340 5.555 |  |
| 49.44-50.2 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.CCC (space-to-Earth) 5.516B 5.554A 5.555B MOBILE | 5.149 5.340 5.555 |
| 50.2-50.4 EARTH EXPLORATION-SATELLITE (passive) SPACE RESEARCH (passive) 5.340 |
| 50.4-51.4 FIXED FIXED-SATELLITE (Earth-to-space) ADD 5.CCC MOBILE Mobile-satellite (Earth-to-space) |

MOD	USA/5A4/12

51.4-55.78 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 51.4-52.6 FIXED ADD 5.CCC MOBILE 5.547 5.556 |
| 52.6-54.25 EARTH EXPLORATION-SATELLITE (passive) SPACE RESEARCH (passive) 5.340 5.556 |

ADD	USA/5A4/13

RESOLUTION  [AI 1.20]  (WRC-07)

Compatibility analyses between the Earth exploration-satellite 
(passive) service and active services above 31 GHz

The World Radiocommunication Conference (Geneva, 2007),

considering

a)	that primary allocations have been made to various space services in the Earth-to-space direction such as the fixed-satellite service, mobile-satellite service and broadcasting-satellite service, and to terrestrial services such as the fixed service, mobile service and broadcasting service, hereafter “active services”, in bands adjacent to or nearby bands allocated to the Earth exploration-satellite (passive) service;

b) 	that unwanted emissions from active services may cause unacceptable interference to the Earth exploration-satellite (passive) service;

c) 	that an administration has adopted domestic regulations to control unwanted emissions including in the bands allocated to the Earth exploration-satellite (passive) service;

d)	that for technical or operational reasons, the general limits in Appendix 3 may be insufficient to protect the Earth exploration-satellite (passive) service in specific bands;

e)	that, in many cases, the frequencies used by the EESS (passive) sensors are chosen to study natural phenomena producing radio emissions at frequencies fixed by the laws of nature, and therefore shifting frequency to avoid or mitigate interference problems may not be possible;

f)	that frequency bands specified in No. 5.340, which prohibits all emissions in those bands, need to be fully protected, as they are unique natural resources;

g)	that the band 31.3-31.5 GHz is used by spaceborne sensors operating in the Earth exploration-satellite (passive) service to obtain measurements of cloud water content and precipitation, and for determining snow and sea ice morphology;

h)	that the band 50.2-50.4 GHz is used by spaceborne sensors operating in the Earth exploration-satellite (passive) service as the indispensable calibration window channel for passive frequencies, which are used to obtain atmospheric temperature profiles, a key component in numerical weather prediction models;

i)	that the band 52.6-54.25 GHz is used by spaceborne sensors operating in the Earth exploration-satellite (passive) service to obtain atmospheric temperature profiles at specific altitudes;

j)	that Report ITU-R SM.2092 provides a methodology for conducting studies, and documents the results of compatibility studies between active and passive services operating in selected pairs of relevant adjacent and nearby bands;

k)	that it is necessary to ensure an equitable burden sharing for achieving compatibility between active and passive services,

recognizing

that, under certain deployment scenarios, the results of simulation studies documented in Report ITU-R SM.2092 have shown that the Earth exploration-satellite service (passive) could be protected:

a)	in the band 31.3-31.5 GHz if the unwanted emissions power in that band delivered to the antenna of fixed service transmitters (except high-altitude platform stations) operating in the band 31-31.3 GHz were not to exceed –38 dBW in any 100 MHz bandwidth;

b)	in the band 50.2-50.4 GHz if the unwanted emissions power in that band delivered to the antenna of earth station transmitters operating in the band 47.2-50.2 GHz or in the band 50.4-51.4 GHz were not to exceed a value between –20 dBW and –10 dBW depending on earth station antenna size;

c)	in the band 52.6-54.25 GHz if the unwanted emissions power in that band delivered to the antenna of fixed service transmitters operating in the band 51.4-52.6 GHz were not to exceed –33 dBW in any 100 MHz bandwidth,

further recognizing

a)	that the fixed service in the bands 31-31.3 GHz and 51.4-52.6 GHz, and the fixed-satellite service (Earth-to-space) in the bands 47.2-50.2 GHz and 50.4-51.4 GHz, are not sufficiently developed to allow a determination of the impact of unwanted emission limits on the fixed and fixed-satellite services in these bands;

b)	that further studies and conference action on this issue are not expected to extend beyond WRC-11,

noting

that long-term protection of the Earth exploration-satellite service in the bands 31.3-31.5 GHz, 50.2-50.4 GHz and 52.6-54.25 GHz is vital to weather prediction and disaster management,

resolves

1	that future conferences should give adequate consideration to the Earth exploration-satellite (passive) service before allocating frequency bands to services with stations transmitting at high elevation angles when those frequency bands are adjacent to or nearby bands allocated to the Earth exploration-satellite (passive) service;

2	that future conferences should give adequate consideration to active services with stations transmitting at high elevation angles before allocating frequency bands to the Earth exploration-satellite (passive) service in adjacent or nearby frequency bands;

3	that, until a future conference resolves the issue of EESS (passive) protection, administrations should take into account the values indicated in the recognizing to protect the EESS (passive), when designing and implementing systems and networks in the bands 31-31.3 GHz, 47.2-50.2 GHz, 50.4-51.4 GHz and 51.4-52.6 GHz;

4	to recommend that WRC-11 review options for protecting the Earth exploration-satellite (passive) service in the bands in resolves 3 on a band-by-band and service-by-service basis, taking into account the results of studies, including those on the impact on all concerned services of implementing or not implementing such options;

5	that all options for the protection of the Earth exploration-satellite (passive) service in the frequency bands 31.3-31.5 GHz, 50.2-50.4 GHz and 52.6-54.25 GHz from unwanted emissions interference, including mandatory or non-mandatory limits on unwanted emissions, or no limits where none are warranted, need to be considered,

invites ITU-R

to undertake further band-by-band analyses, given the unique characteristics of each band,

invites administrations

1	to provide the relevant characteristics of fixed service systems in the bands 31-31.3 GHz and 51.4-52.6 GHz, and fixed-satellite service (Earth-to-space) systems in the bands 47.2-50.2 GHz and 50.4-51.4 GHz;

2	to actively participate in the studies identified in invites ITU-R.

Reasons:	The fixed service in the bands 31-31.3 GHz and 51.4-52.6 GHz, and the fixed-satellite service (Earth-to-space) in the bands 47.2-50.2 GHz and 50.4-51.4 GHz, are not sufficiently developed to allow a determination of the impact of unwanted emission limits on the fixed and fixed-satellite services in these bands prior to WRC-07. A compromise proposal is made pending further consideration at a future WRC of the issue of protecting the Earth exploration-satellite (passive) service from unwanted emissions from active services operating above 31 GHz.

SUP	USA/5A4/14

RESOLUTION  738  (WRC-03)

Compatibility analyses between the Earth exploration-satellite 
service (passive) and active services

Reasons:	Resolution [AI 1.20] (WRC-07) replaces Resolution 738 (WRC-03).

____________

# Footnotes

1	Protection values are contained in Resolution 738 considering f) and g) as follows:

“f)	that according to Recommendation ITU-R SM.1633, the EESS (passive) in the band 31.3-31.5 GHz can be protected if the unwanted emissions of fixed-service systems (except high-altitude platform stations (HAPS)) operating in the band 31.0-31.3 GHz do not exceed –38 dBW in a 100 MHz reference bandwidth in the band 31.3-31.5 GHz;

g)	that according to Recommendation ITU-R SM.1633, the EESS (passive) in the band 52.6-54.25 GHz can be protected if the unwanted emissions of fixed-service systems operating in the band 51.4-52.6 GHz do not exceed –33 dBW in a 100 MHz reference bandwidth in the band 52.6-54.25 GHz;”.