| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 20 to Document 41-E |
|  | 22 August 2007 |
|  | Original: English |
| Asia-Pacific Telecommunity Administrations |
| common proposals for the work of the conference |
| Agenda item 1.20 |

1.20	to consider the results of studies, and proposals for regulatory measures if appropriate regarding the protection of the EESS (passive) from unwanted emissions of active services in accordance with Resolution 738 (WRC-03)

Introduction

WRC-07 Agenda item 1.20 addresses the compatibility between the Earth exploration-satellite service (EESS) (passive) and active services in adjacent or nearby bands as specified in Resolution 738 (WRC-03). The results of the studies carried out for each band pair under this agenda item are documented in Report ITU-R SM.2092, which replaces Recommendation ITU-R SM.1633 for the purpose of this Resolution.

Based on the results of these studies, regulatory measures to ensure protection of the EESS (passive) from unwanted emissions of active services may be considered, while taking into account the impact on all concerned services of implementing or not implementing such measures.

For each band pair studied, the appropriate method to satisfy the agenda item may be decided independently. In addition to the methods described below, the Conference may decide that, for a given band pair, no regulatory measures are required.

One method is to establish, in an EESS (passive) band, a mandatory power limit for unwanted emissions from a single transmitter of a specified service in an adjacent or nearby band without examination by the Bureau. Another method is to establish, in an EESS (passive) band, a non-mandatory power limit for unwanted emissions from a single transmitter of a specified service in an adjacent or nearby band. The third method is to strongly encourage administrations to take all practicable steps to limit unwanted emissions in EESS (passive) bands from active services in adjacent and nearby frequency bands.

APT members support the ITU-R studies regarding the compatibility analyses for each band pair under this agenda item, which were documented in Report ITU-R SM.2092. APT members support the considerations described in the CPM Report on WRC-07 Agenda item 1.20 that the regulatory measures for regulating unwanted emissions from active services should be appropriately determined for each band pair independently taking into account the results of the ITU-R studies.

The expressed consensus is in favour of establishing, in the following active services bands, a mandatory power limit for unwanted emissions in EESS (passive) bands from a single transmitter of a specified service. However, it is the opinion of APT members that the mandatory power limits will only be applicable for active systems brought into use after a future date to be decided by WRC-07.

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	ASP/41A20/322

1 300-1 525 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 1 427-1 429 SPACE OPERATION (Earth-to-space) ADD 5.A120 FIXED MOBILE except aeronautical mobile 5.341 |

ADD	ASP/41A20/323

5.A120	Stations in the space operation service (Earth-to-space) in the band 1 427-1 429 MHz shall operate in accordance with the provisions of Resolution [ASP/AI1.20/1-EESS (PASSIVE)] (WRC-07).     (WRC-07)

Reasons:	Studies in Report ITU-R SM.2092 indicate that EESS (passive) systems in the 1 400-1 427 MHz band are protected if unwanted emissions in that band from space operation service (Earth-to-space) transmitters in the 1 427-1 429 MHz band do not exceed –36 dBW in any 27 MHz reference bandwidth. Measures to ensure that future space operation service (Earth-to-space) transmitters in the 1 427-1 429 MHz band do not exceed this level will not constitute an undue burden on the space operation service.

MOD	ASP/41A20/324

22-24.75 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 22.55-23.55 FIXED INTER-SATELLITE ADD 5.B120 MOBILE 5.149 |

ADD	ASP/41A20/325

5.B120	Stations in the inter-satellite service (non-GSO only) in the band 22.55-23.55 GHz shall operate in accordance with the provisions of Resolution [ASP/AI1.20/1-EESS (PASSIVE)] (WRC-07).     (WRC-07)

Reasons:	Studies in Report ITU-R SM.2092 indicate that EESS (passive) systems in the 23.6-24 GHz band are protected if unwanted emissions in that band from inter-satellite service non-GSO transmitters in the 22.55-23.55 GHz band do not exceed –46 dBW in any 200 MHz reference bandwidth. Measures to ensure that future non-GSO inter-satellite service systems in the 22.55-23.55 GHz band do not exceed this level will not constitute an undue burden on the inter-satellite service.

The simulations of the ISS links in the GSO data relay systems indicate in Report ITU-R SM.2092 that the permissible interference criteria of Recommendation ITU-R RS.1029-2 will be satisfied for all the passive sensors.

MOD	ASP/41A20/326

29.9-34.2 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 31-31.3 FIXED 5.543A ADD 5.C120 MOBILE Standard frequency and time signal-satellite (space-to-Earth) Space research 5.544 5.545 5.149 |

ADD	ASP/41A20/327

5.C120	Stations in the fixed service (except HAPS) in the band 31-31.3 GHz shall operate in accordance with the provisions of Resolution [ASP/AI1.20/1-EESS (PASSIVE)] (WRC-07).
(WRC-07)

Reasons:	Studies in Report ITU-R SM.2092 indicate that EESS (passive) systems in the 31.3-31.5 GHz band are protected if unwanted emissions in that band from fixed service (except HAPS) transmitters in the 31.0-31.3 GHz band do not exceed –38 dBW in any 100 MHz reference bandwidth. Measures to ensure that future FS systems in the 31.0-31.3 GHz band do not exceed this level will not constitute an undue burden on the fixed service.

MOD	ASP/41A20/328

40-47.5 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 47.2-47.5 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.D120 MOBILE 5.552A |

MOD	ASP/41A20/328A

47.5-51.4 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 47.5-47.9 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 (space-to-Earth) 5.516B 5.554A MOBILE | 47.5-47.9 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.D120 MOBILE |
| 47.9-48.2 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.D120 MOBILE 5.552A |
| 48.2-48.54 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 (space-to-Earth) 5.516B 5.554A 5.555B MOBILE | 48.2-50.2 FIXED FIXED-SATELLITE (Earth-to-space) 5.516B 5.552 ADD 5.D120 MOBILE |
| 48.54-49.44 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 MOBILE 5.149 5.340 5.555 |  |
| 49.44-50.2 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.D120 (space-to-Earth) 5.516B 5.554A 5.555B MOBILE | 5.149 5.340 5.555 |
| 50.2-50.4 EARTH EXPLORATION-SATELLITE (passive) SPACE RESEARCH (passive) 5.340 |
| 50.4-51.4 FIXED FIXED-SATELLITE (Earth-to-space) ADD 5.D120 MOBILE Mobile-satellite (Earth-to-space) |

ADD	ASP/41A20/329

5.D120	Stations in the fixed-satellite service (Earth-to-space) in the bands 47.2-50.2 GHz (Regions 2 and 3), 49.44-50.2 GHz (Region 1), and 50.4-51.4 GHz shall operate in accordance with the provisions of Resolution [ASP/AI1.20/1-EESS (PASSIVE)] (WRC-07).     (WRC-07)

Reasons:	Studies in Report ITU-R SM.2092 indicate that EESS (passive) systems in the 50.2-50.4 GHz band are protected if unwanted emissions in that band from fixed-satellite service transmitters in the 47.2-50.2 GHz band do not exceed –20 to –10 dBW in any 200 MHz reference bandwidth. Measures to ensure that future fixed-satellite service systems in the 47.2-50.2 GHz band do not exceed this level will not constitute an undue burden on the fixed service.

Studies in Report ITU-R SM.2092 indicate that EESS (passive) systems in the 50.2-50.4 GHz band are protected if unwanted emissions in that band from fixed-satellite service transmitters in the 50.4-51.4 GHz band do not exceed –20 to –10 dBW in any 200 MHz reference bandwidth. Measures to ensure that future fixed-satellite service systems in the 50.4-51.4 GHz band do not exceed this level will not constitute an undue burden on the fixed service.

MOD	ASP/41A20/330

51.4-55.78 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 51.4-52.6 FIXED ADD 5.E120 MOBILE 5.547 5.556 |

ADD	ASP/41A20/331

5.E120	Stations in the fixed service in the band 51.4-52.6 GHz shall operate in accordance with the provisions of Resolution [ASP/AI1.20/1-EESS (PASSIVE)] (WRC-07).     (WRC-07)

Reasons:	Studies documented in Report ITU-R SM.2092 indicate that EESS (passive) systems in the 52.6-54.25 GHz band are protected if unwanted emissions in that band from fixed service transmitters in the 51.4-52.6 GHz band do not exceed –33 dBW in any 100 MHz reference bandwidth. Measures to ensure that future FS systems in the 51.4-52.6 GHz band do not exceed this level will not constitute an undue burden on the fixed service.

MOD	ASP/41A20/332

5.340	All emissions are prohibited in the following bands:

1 400-1 427 MHz,

2 690-2 700 MHz,	except those provided for by No. 5.422,

10.68-10.7 GHz,	except those provided for by No. 5.483,

15.35-15.4 GHz,	except those provided for by No. 5.511,

23.6-24 GHz,

31.3-31.5 GHz,

31.5-31.8 GHz,	in Region 2,

48.94-49.04 GHz,	from airborne stations

50.2-50.4 GHz,

52.6-54.25 GHz,

86-92 GHz,

100-102 GHz,

109.5-111.8 GHz,

114.25-116 GHz,

148.5-151.5 GHz,

164-167 GHz,

182-185 GHz,

190-191.8 GHz,

200-209 GHz,

226-231.5 GHz,

250-252 GHz.     (WRC-03)

Reasons:	After the proposed Resolution [EESS (PASSIVE)] is approved, No. 5.340.1 needs to be suppressed.

ADD	ASP/41A20/333

RESOLUTION [ASP/AI1.20/1-EESS (passive)] (WRC-07)

Compatibility between the Earth exploration-satellite 
service (passive) and active services

The World Radiocommunication Conference (Geneva, 2007),

considering

a)	that primary allocations have been made to various space services in the Earth-to-space direction such as the fixed-satellite service, space operation service, inter-satellite service and/or to terrestrial services such as the fixed service, mobile service and radiolocation service, hereafter referred to as “active services”, in bands adjacent or nearby to bands allocated to the Earth exploration-satellite service (EESS) (passive);

b)	that unwanted emissions from active services may cause unacceptable interference to the EESS (passive);

c)	that for technical or operational reasons, the general limits in Appendix 3 may be insufficient in protecting the EESS (passive) in specific bands;

d)	that, in many cases, the frequencies used by the EESS (passive) sensors are chosen to study natural phenomena producing radio emissions at frequencies fixed by the laws of nature, and therefore shifting frequency to avoid or mitigate interference problems may not be possible;

e)	that it is necessary to ensure an equitable burden sharing for achieving compatibility between active and passive services operating in adjacent or nearby bands,

noting

a)	that frequency bands covered by No. 5.340 which prohibits all emissions need to be fully protected as they are unique natural resources;

b)	that Report ITU-R SM.2092 provides a methodology for conducting the compatibility studies between active and passive services operating in adjacent and nearby bands and develops all relevant scenarios;

c)	that Recommendation ITU-R RS.1029-2 provides the permissible interference criteria for satellite passive remote sensing,

resolves

1	that unwanted emissions from stations, brought into use after [effective date of WRC-07 Final Acts], in the bands and services listed in Table 1, shall not exceed the corresponding limits in that table;

2	that the Bureau shall make no examination or finding with respect to this Resolution under either Article 9 or 11.

TABLE 1

| Passive band | Active band | Active service | The maximum power density delivered to the antenna of a station in the passive band |
| --- | --- | --- | --- |
| 1 400-1 427 MHz | 1 427-1 429 MHz | SOS | –36 dB(W/27 MHz) |
| 23.6-24 GHz | 22.55-23.55 GHz | ISS (non-GSO only) | –46 dB(W/200 MHz) |
| 31.3-31.5 GHz | 31-31.3 GHz | FS (except HAPS) | –38 dB(W/100 MHz) |
| 50.2-50.4 GHz | 47.2-50.2 GHz (Regions 2 and 3) | FSS (Earth-to-space) | –10 dB(W/200 MHz) |
| 50.2-50.4 GHz | 49.44-50.2 GHz (Region 1) |  |  |
| 50.2-50.4 GHz | 50.4-51.4 GHz | FSS (Earth-to-space) | –10 dB(W/200 MHz) |
| 52.6-54.25 GHz | 51.4-52.6 GHz | FS | –33 dB(W/100 MHz) |

Reasons:	See ADD ASP/41A20/323, 325, 327, 329 and 331.

______________