| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 12 to Document 43-E |
|  | 3 September 2007 |
|  | Original: English |
| African Telecommunications Union Administrations |
| AFRICAN COMMON Proposals for the work of the Conference |
| Agenda item 1.7 |

1.7	to consider the results of ITU-R studies regarding sharing between the mobile-satellite service and the SRS (passive) in the band 1 668-1 668.4 MHz, and between the mobile-satellite service and the mobile service in the band 1 668.4-1 675 MHz in accordance with Resolution 744 (WRC-03)

Introduction

Issue A deals with sharing between the mobile-satellite service (Earth-to-space) and the space research (passive) service in the band 1 668-1 668.4 MHz.

Issue B deals with sharing between the mobile-satellite service (Earth-to-space) and the fixed and mobile services in the band 1 668.4-1 675 MHz.

Proposals for Agenda item 1.7

No common proposal on Issue A.

AFCP/43A12/1

For Issue B, the African administrations support Method B1, which calls for a hard limit to be placed on the e.i.r.p. spectral density of transportable radio-relay stations.

Reasons:	Provides adequate protection of the MSS from interference from the MS for single-entry interference cases.

______________