| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 18 to Document 43-E |
|  | 3 September 2007 |
|  | Original: English |
| African Telecommunications Union Administrations |
| african common proposals for the work of the conference |
| Agenda item 1.20 |

1.20	to consider the results of studies, and proposals for regulatory measures if appropriate regarding the protection of the EESS (passive) from unwanted emissions of active services in accordance with Resolution 738 (WRC-03)

# The band 1 400-1 427 MHz

AFCP/43A18/1

The African Administrations support Method B of the CPM Report for the band 1 400-1 427 MHz establishing non-mandatory power limits for unwanted emissions. A new footnote should be added in RR Article 5 which would recommend the use of maximum levels of unwanted emissions for this band provided in a new WRC-07 Resolution. These limits should be derived from the relevant parts of Report ITU-R SM.2092 and Recommendation ITU-R SM.329.

AFCP/43A18/2

Develop a new WRC-07 Resolution that should contain the following resolves:

“that administrations are urged to take all reasonable steps to ensure that stations, brought into use after 1 January 20XY, in the band 1 400-1 427 MHz and services listed in Table X, comply with the limits contained in Table X.”

Reasons:	It is desirable to provide a certain level of protection for the EESS (passive) system as well as flexibility for administrations in regulating unwanted emissions in the 1 400-1 427 MHz band.

# The bands 23.6-24 GHz, 31.3-31.5 GHz and 50.2-50.4 GHz

AFCP/43A18/3

The African Administrations support Method A of the CPM Report establishing mandatory power limits for unwanted emissions for the bands 23.6-24 GHz, 31.3-31.5 GHz and 50.2-50.4 GHz. A new footnote should be added in RR Article 5 similar to RR No. 5.347A that would require compliance with unwanted emission limits in a new Resolution. This Resolution would provide the limits of unwanted emissions in the 23.6-24 GHz, 31.3-31.5 GHz and 50.2-50.4 GHz bands derived from the relevant parts of Report ITU-R SM.2092 and Recommendation ITU-R SM.329.

Reasons:	Taking into account the importance of information derived by passive sensors operating in these frequency bands for providing an “all-weather” capability many African Administrations support regulatory measures for the protection of the EESS (passive) from unwanted emissions of active services.

____________