| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 2 to Document 43-E |
|  | 3 September 2007 |
|  | Original: English |
| African Telecommunications Union Administrations |
| AFRICAN COMMON Proposals for the work of the Conference |
| Agenda item 1.3 |

1.3	in accordance with Resolution 747 (WRC-03), consider upgrading the radiolocation service to primary allocation status in the bands 9 000-9 200 MHz and 9 300-9 500 MHz and extending by up to 200 MHz the existing primary allocations to the Earth exploration-satellite service (EESS) (active) and the space research service (SRS) (active) in the band 9 500-9 800 MHz without placing undue constraint on the services to which the bands are allocated

Resolution 747 (WRC-03) – Possible upgrade of the radiolocation service to primary allocation status in the frequency bands 9 000-9 200 MHz and 9 300-9 500 MHz, and possible extension of the existing primary allocations to the Earth exploration-satellite service (active) and the space research service (active) in the band 9 500-9 800 MHz

Resolution 747 (WRC-03), further resolves 1

Introduction

African administrations support upgrading the allocation to the radiolocation service in the bands 9 000-9 200 MHz and 9 300-9 500 MHz to a primary service with the addition of a new footnote to protect existing services and modification of No. 5.475.

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	AFCP/43A2/1

8 500-10 000 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 9 000-9 200 AERONAUTICAL RADIONAVIGATION 5.337 RADIOLOCATION 5.471 ADD 5.A03 |
| 9 200-9 300 RADIOLOCATION MARITIME RADIONAVIGATION 5.472 5.473 5.474 |
| 9 300-9 500 RADIONAVIGATION 5.476 RADIOLOCATION 5.427 5.474 MOD 5.475 ADD 5.A03 |

ADD	AFCP/43A2/2

5.A03	In the bands 9 000-9 200 MHz and 9 300-9 500 MHz, stations operating in the radiolocation service shall not cause harmful interference to, nor claim protection from, systems operating in the aeronautical radionavigation service. In the band 9 300-9 500 MHz, ground-based radars used for meteorological purposes have priority over their radiolocation devices.

MOD	AFCP/43A2/3

5.475	The use of the band 9 300-9 500 MHz by the aeronautical radionavigation service is limited to airborne weather radars and ground-based radars. In addition, ground-based radar beacons in the aeronautical radionavigation service are permitted in the band 9 300-9 320 MHz on condition that harmful interference is not caused to the maritime radionavigation service.

Reasons:	The tests and studies carried out show compatibility between the radiolocation and radionavigation systems. The upgrade will provide a primary allocation to the radiolocation service, contiguous across 8.5-10.5 GHz, with sufficient bandwidth to meet emerging requirements for increased image resolution and increased range accuracy. It also provides an explicit requirement for protection of the radionavigation system through continued priority of the radionavigation system over radiolocation service.

Resolution 747 (WRC-03), further resolves 2

Introduction

African administrations support the provision of a primary allocation to the EESS (active) and SRS (active) in the band 9 300-9 500 MHz, extending the current No. 5.476A and indicating that this extension is limited to systems that need bandwidth wider than the bandwidth available within the existing allocation from 9 500-9 800 MHz.

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	AFCP/43A2/4

8 500-10 000 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 9 300-9 500 RADIONAVIGATION 5.476 Radiolocation EARTH EXPLORATION-SATELLITE (active) ADD 5.B03 SPACE RESEARCH (active) ADD 5.B03 5.427 5.474 5.475 MOD 5.476A |
| 9 500-9 800 EARTH EXPLORATION-SATELLITE (active) RADIOLOCATION RADIONAVIGATION SPACE RESEARCH (active) MOD 5.476A |
| 9 800-10 000 RADIOLOCATION Fixed 5.477 5.478 5.479 |

ADD	AFCP/43A2/5

5.B03	The use of the band 9 300-9 500 MHz by EESS (active) and SRS (active) is limited to systems that cannot be accommodated within the 9 500-9 800 MHz band and that require bandwidths larger than 300 MHz.

MOD	AFCP/43A2/6

5.476A	In the band 9 300-9 800 MHz, stations in the Earth exploration-satellite service (active) and space research service (active) shall not cause harmful interference to stations of the radionavigation and radiolocation services.     (WRC-07)

Reasons:	This method provides additional 200 MHz primary allocation for EESS (active) and SRS (active) in order to greatly improve the resolution of the features that would operate contiguously across 9 300-9 800 MHz for global monitoring and for environmental and land-use purposes. It also provides an explicit requirement for the protection of radionavigation and radiolocation systems. It also avoids an extension of the allocation to narrow-band EESS active systems (less than 300 MHz bandwidth) that may present higher interference potential against radiodetermination systems.

______________