| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 7 to Document 43-E |
|  | 3 September 2007 |
|  | Original: English |
| African Telecommunications Union Administrations |
| AFRICAN COMMON Proposals for the work of the Conference |
| Agenda item 1.10 |

1.10	to review the regulatory procedures and associated technical criteria of Appendix 30B without any action on the allotments, the existing systems or the assignments in the List of Appendix 30B

AFCP/43A7/1

The African administrations support the modernization of the Appendix 30B, taking into consideration the results of the ITU-R studies, relating to the latest advancement in technology with a view to properly respond to the principle of the efficient, rational and effective use of the orbital and the spectrum resources.

The African countries consider that the review of Appendix 30B of the Radio Regulations should be based upon the following principles:

1	Appendix 30B of the ITU Radio Regulations should remain an allotment plan, with one orbital position for each country, except for those countries for which more than one orbital position was assigned at WARC-Orb 88. Similarly, this allotment Plan must continue to have an associated 800 MHz of spectrum as it has been the case up to now.

2	Any administration shall retain the right to comment in respect of their own allotments and/or assignments.

3	The Plan must provide a guaranteed equitable access (orbit/spectrum), in an equitable manner.

4	The Plan shall limit its scope to a national coverage with the possibility that administrations could conclude an agreement among themselves, in order to:

–	share their orbital/spectrum resources in the Plan, and/or

–	establish subregional systems on an economical and cost-effective basis, and/or

–	apply for additional uses under certain conditions as established in Appendix 30B of the Radio Regulations.

5	The concept of a predetermined arc (PDA) should be maintained, preferably in conjunction with the coordination arc concept.

6	The Plan must take into consideration appropriate interference criteria for identification of affected administrations, as currently contained in Appendix 30B of the Radio Regulations.

7	The concept of operation under “non-interference non-protection” basis, is not accepted by the African countries.

8	Whenever interference occurs to an existing network, an explicit agreement of the affected administration(s) is to be obtained. Non reply should not constitute an agreement according to current practice.

9	The flexibility should be maintained in the review of Appendix 30B in order to allow sufficient margin in the Plan in terms of the established C/I compared to actually required C/I, in order to have sufficient margin to reduce their antenna diameter or other criteria, for the easy conversion of the allotment into assignments.

10	All allotments should be recalculated taking into account the new technical parameters adopted by the conference.

11	The calculation of single-entry and aggregate C/I for all test points must be based on the combination of uplink and downlink without separating the two links, provided that both links are in the planned bands.

12	Protection should be ensured all over the territory of any administration, not only on a few test points over the territory of such administration.

13	All required technical and regulatory examinations should be carried out by the Bureau as is the current practice.

The African administrations are open to any new proposal submitted to the Conference aligned with the principles stated above and showing improvement in the reduction of the ITU backlog. Furthermore, the following issues are emphasized:

–	The principle of the Plan guaranteeing equitable access to orbital position and to associated frequency bands by any administration shall be maintained. (cf.: Article 1 and Article 11 of Appendix 30B of the Radio Regulations).

–	The African administration assets, as included in the List or under processing, should be properly preserved.

–	All consequences of any change of Appendix 30B should be clearly identified and measured by the Conference.

______________