| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 16 to Document 10-E |
|  | 11 May 2007 |
|  | Original: English |
| EUROPEAN COMMON PROPOSALS FOR THE WORK OF THE CONFERENCE |
| PART 16 |
| Agenda item 1.16 |

1.16	to consider the regulatory and operational provisions for Maritime Mobile Service Identities (MMSIs) for equipment other than shipborne mobile equipment, taking into account Resolutions 344 (Rev.WRC-03) and 353 (WRC-03)

Introduction

Europe proposes amendments to Article 19 of the Radio Regulations to allow for the assignment of MMSIs to search and rescue (SAR) aircraft, aids to navigation and craft associated with a parent ship.

ARTICLE  19

Identification of stations

Section II  –  Allocation of international series and assignment of call signs

MOD	EUR/10A16/1

19.30		2)	As the need arises, ship stations and ship earth stations to which the provisions of Chapter IX apply, and coast stations, coast earth stations, aircraft stations, aids to navigation or craft associated with a parent ship capable of communicating with such ship stations, shall have assigned to them maritime mobile service identities in accordance with Section VI of this Article.

Reasons:	Modification EUR/10A16/1 expands the current MMSI definition to include aircraft stations, aids to navigation and craft associated with a parent ship.

MOD	EUR/10A16/2

Section VI  –  Maritime mobile service identities

Reasons:	Simplify the title.

MOD	EUR/10A16/3

19.99	§ 39	When a station5 in the maritime mobile service or the maritime mobile-satellite service is required to use maritime mobile service identities, the responsible administration shall assign the identity to the station in accordance with the provisions described in Nos. 19.100 to 19.126J; in so doing, it should take into account the relevant ITU-R and ITU-T Recommendations. In accordance with No. 20.16, administrations shall notify the Bureau immediately when assigning maritime mobile service identities

Reasons:	Consequential change resulting from the addition of provisions 19.126A to 19.126J.

MOD	EUR/10A16/4

19.100	§ 40	1)	Maritime mobile service identities are formed of a series of nine digits which are transmitted over the radio path in order to uniquely identify ship stations, ship earth stations, coast stations, coast earth stations, group calls, aircraft stations, aids to navigation and craft associated with a parent ship.

MOD	EUR/10A16/5

19.102		3)	There are six kinds of maritime mobile service identities:

MOD	EUR/10A16/6

19.107	v)	identities for aircraft communicating with stations in the maritime mobile service for search and rescue purposes;

ADD	EUR/10A16/7

19.107A	vi)	aids to navigation and craft associated with a parent ship.

Reasons:	Modifications EUR/10A16/2 to EUR/10A16/6 and addition EUR/10A16/7 expand the current MMSI definition to include aircraft stations, aids to navigation and craft associated with a parent ship.

MOD	EUR/10A16/8

19.108A	§ 41	The maritime identification digits M1I2D3 are an integral part of the maritime mobile service identity and denote the geographical area of the administration responsible for the station so identified (see Nos. 19.102 to 19.107A).     (WRC-03)

Reasons:	Consequential change resulting from the modification of provision 19.107 and the addition of provision No. 19.107A.

ADD	EUR/10A16/9

19.126A	G  –  Identities for aircraft

ADD	EUR/10A16/10

19.126B	§ 46bis	1)	When an aircraft is required to use maritime mobile service identities for the purposes of conducting search and rescue communications with stations in the maritime mobile service, the responsible administration shall assign a 9-digit code formed as follows:

111213M4I5D6X7X8X9

where the first three figures are ones and X is any figure from 0 to 9.

ADD	EUR/10A16/11

19.126C		2)	The MID represents only the territory or geographical area of the administration assigning identity for aircraft.

ADD	EUR/10A16/12

19.126D		3)	The combination 111213M4I5D6070809 may be used for a group aircraft identity to all search and rescue aircraft of an administration, where the last three figures are zeros.

Reasons:	Additions EUR/10A16/9 to EUR/10A16/12 introduce provisions for MMSI assignments to SAR aircraft and define a unique format to distinguish these stations from ships, coast stations, aids to navigation and craft associated with a parent ship. Proposed format accommodates the assignment of up to 999 MMSIs per MID for SAR aircraft stations and only prevents the allocation of one MID from the available MID resource.

ADD	EUR/10A16/13

19.126E	H  –  Aids to navigation and craft associated with a parent ship

ADD	EUR/10A16/14

19.126F	§ 46B	1)	When a means of automatic identification is required for a station aiding navigation at sea, the responsible administration shall assign a 9-digit code formed as follows:

9192M3I4D5X6X7X8X9

where the first two figures are nines and X is any figure from 0 to 9.

ADD	EUR/10A16/15

19.126G		2)	The MID represents only the territory or geographical area of the administration assigning the call identity for the navigational aid.

Reasons:	Additions EUR/10A16/13 to EUR/10A16/15 introduce provisions for MMSI assignments to aids to navigation and define a unique format to distinguish these stations from ships, coast stations, aircraft stations and craft associated with a parent ship. Proposed format accommodates the assignment of up to 10 000 MMSIs per MID for aids to navigation.

ADD	EUR/10A16/16

19.126H		3)	Devices located in lifeboats, life rafts and other craft, belonging to a parent ship, the administration concerned shall assign a 9-digit code formed as follows:

9182M3I4D5X6X7X8X9

where the first two figures are nine and eight respectively and X is any figure from 0 to 9.

ADD	EUR/10A16/17

19.126I		4)	These MMSI should be associated with the MMSI of a parent ship by means of database registration.

ADD	EUR/10A16/18

19.126J		5)	The MID represents only the territory or geographical area of the administration assigning the call identity for the craft associated with a parent ship.

Reasons:	Additions EUR/10A16/16 to EUR/10A16/18 introduce provisions for MMSI assignments to craft associated with another vessel and define a unique format to distinguish these stations from ships, coast stations, aircraft stations and aids to navigation. Proposed format accommodates the assignment of up to 10 000 MMSIs per MID for craft associated with a parent ship.

______________

# Footnotes

5 	19.99.1	In this Section a reference to a ship station or a coast station may include the respective earth stations.