| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 9 to Document 10-E |
|  | 14 May 2007 |
|  | Original: English |
| EUROPEAN COMMON PROPOSALS FOR THE WORK OF THE CONFERENCE |
| PART 9 |
| Agenda item 1.9 |

1.9	to review the technical, operational and regulatory provisions applicable to the use of the band 2 500-2 690 MHz by space services in order to facilitate sharing with current and future terrestrial services without placing undue constraint on the services to which the band is allocated

Review of the provisions in the band 2 500-2 690 MHz

Introduction

The band 2 500-2 690 MHz was identified by WRC-2000 for IMT-2000. In CEPT, the band 2 500-2 690 MHz is designated for terrestrial IMT-2000/UMTS systems through ECC decisions DEC(02)06 and DEC(05)05. The band is currently used by a variety of applications such as ENG/OB (programme-making), wireless local loop and point-to-point systems and it will be made available for terrestrial IMT-2000/UMTS by 1 January 2008.

WRC-03 decisions, under former Agenda item 1.34, reviewed the technical and regulatory provisions applicable to non-GSO and GSO BSS (sound) systems in the band 2 605-2 655 MHz in a limited number of countries listed in RR footnotes Nos. 5.418 and 5.417A in order to allow the introduction of BSS (sound) systems in these countries whilst safeguarding the current and planned use of this band by terrestrial services, and in particular IMT-2000 systems, in most countries over the world. The protection of terrestrial systems from BSS (sound) interference was achieved by adopting new regulatory and technical provisions included in the revisions of Resolution 539, No. 5.418 and Appendix 5 and new footnote No. 5.417A. It is worthwhile saluting and recognizing the mutual understanding efforts that helped coming to this decision. WRC-07 Agenda item 1.9 conclusions should therefore not modify the solution that was elaborated on WRC-03 Agenda item 1.34.

The technical and regulatory studies that addressed the sharing between BSS (sound) systems and terrestrial systems in the band 2 605-2 655 MHz under WRC-03 Agenda item 1.34, highlighted the fact that the technical and regulatory provisions currently applicable to space services allocated in the band 2 500-2 690 MHz, do not provide efficient safeguard to the current and future terrestrial systems in the band 2 500-2 690 MHz. WRC-07 Agenda item 1.9 was proposed in this context. The scope of Agenda item 1.9 is limited to the review of the technical, operational and regulatory provisions applicable to transmit space stations in the band 2 500-2 690 MHz in order to protect terrestrial stations in the fixed and mobile services. The review of technical, operational and regulatory provisions applicable to terrestrial services in order to protect satellite systems in the band 2 500-2 690 MHz are out of the scope of this agenda item.

Studies under Agenda item 1.9 confirmed that the current regulatory situation applicable to space services allocated in the band 2 500-2 690 MHz do not provide the required protection to the current and future terrestrial systems in the band 2 500-2 690 MHz. In particular, the current power flux-density limits applicable to space services would lead to interference into IMT-2000 systems considerably above the appropriate sharing criteria. It is therefore necessary to tighten these values to safeguard terrestrial systems including IMT-2000 systems, further development of IMT-2000 and IMT-Advanced in the band 2 500-2 690 MHz.

The hard limit regulatory regime based on the specification of a power flux-density mask in Article 21 of the Radio Regulations, would be the regulatory regime that ensures the long-term safeguard of terrestrial systems in the band 2 500-2 690 MHz from satellite interference, while providing long-term visibility for space systems to be developed within a clear predefined framework.

Based on the conclusions of the studies and discussions held within CEPT, Europe proposes:

1)	To define power-flux density (pfd) limits in Article 21 applicable to all space services, except BSS (sound), having an allocation in the frequency band 2 500-2 690 MHz.

2)	To set these pfd limits to the following values, in dB(W/m2/MHz):

–133			for	 0	≤ θ ≤ 5°

–133 + 8/20*(θ – 5)	for	 5	≤ θ ≤ 25°

–125			for	25	≤ θ ≤ 90°

with θ the angle of arrival above the horizontal plane.

3)	To not review conclusions of WRC-03 for what concerns BSS (sound) in the band 2 605-2 655 MHz.

4)	To consider the date of application of the new provisions as an important issue and to consider that a suitable solution may be for the proposed new limits to apply to any satellite systems or networks operating in the 2 500-2 690 MHz band except those for which complete notification information has been received by the Radiocommunication Bureau before 17 November 2007, and whose frequency assignments in the 2 500-2 690 MHz band were brought into use by 31 December 2008 (the existing limits shall continue to apply to these latter systems).

Moreover, No. 9.19 of the Radio Regulations provides that coordination shall be effected by any transmitting station of a terrestrial service in a frequency band shared on an equal primary basis with the broadcasting-satellite service, with respect to typical earth stations included in the service area of a space station in the broadcasting-satellite service.

According to Table 5-1 of Appendix 5, one of the frequency bands, to which No. 9.19 applies, is the band 2 535-2 655 MHz. According to the same table, No. 9.19 does not apply to the bands 2 520-2 535 MHz and 2 655-2 670 MHz although they are both allocated to the broadcasting-satellite service.

The intention of Europe is to remove any necessity for coordination of the terrestrial services, including IMT-2000 and systems beyond with the typical earth stations of the broadcasting-satellite service in frequency band 2 520-2 670 MHz.

Therefore, given that the provisions of No. 9.19 may place undue constraints on the terrestrial services in the band 2 520-2 670 MHz band, where major developments in the terrestrial services are foreseen, it is proposed to deactivate its application in this band.

Taking into account the above proposals the Radio Regulations would be amended as follows:

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	EUR/10A9/1

2 170-2 520 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 2 500-2 520 FIXED 5.409 5.410 5.411 MOBILE except aeronautical mobile 5.384A MOBILE-SATELLITE (space-to-Earth) 5.351A MOD 5.403 | 2 500-2 520 FIXED 5.409 5.411 FIXED-SATELLITE (space-to-Earth) MOD 5.415 MOBILE except aeronautical mobile 5.384A MOBILE-SATELLITE (space-to-Earth) 5.351A MOD 5.403 |
| 5.405 5.407 5.412 MOD 5.414 | 5.404 5.407 MOD 5.414 5.415A |

MOD	EUR/10A9/2

2 520-2 700 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 2 520-2 655 FIXED 5.409 5.410 5.411 MOBILE except aeronautical mobile 5.384A BROADCASTING-SATELLITE 5.413 MOD 5.416 | 2 520-2 655 FIXED 5.409 5.411 FIXED-SATELLITE (space-to-Earth) MOD 5.415 MOBILE except aeronautical mobile 5.384A BROADCASTING-SATELLITE 5.413 MOD 5.416 | 2 520-2 535 FIXED 5.409 5.411 FIXED-SATELLITE (space-to-Earth) MOD 5.415 MOBILE except aeronautical mobile 5.384A BROADCASTING-SATELLITE 5.413 MOD 5.416 |
|  |  | MOD 5.403 5.415A |
|  |  | 2 535-2 655 FIXED 5.409 5.411 MOBILE except aeronautical mobile 5.384A BROADCASTING-SATELLITE 5.413 MOD 5.416 |
| 5.339 MOD 5.403 5.405 5.412 5.417C 5.417D 5.418B 5.418C | 5.339 MOD 5.403 5.417C 5.417D 5.418B 5.418C | 5.339 5.417A 5.417B 5.417C 5.417D 5.418 5.418A 5.418B 5.418C |
| 2 655-2 670 FIXED 5.409 5.410 5.411 MOBILE except aeronautical mobile 5.384A BROADCASTING-SATELLITE 5.347A 5.413 MOD 5.416 Earth exploration-satellite (passive) Radio astronomy Space research (passive) | 2 655-2 670 FIXED 5.409 5.411 FIXED-SATELLITE (Earth-to-space) (space-to-Earth) 5.347A MOD 5.415 MOBILE except aeronautical mobile 5.384A BROADCASTING-SATELLITE 5.347A 5.413 MOD 5.416 Earth exploration-satellite (passive) Radio astronomy Space research (passive) | 2 655-2 670 FIXED 5.409 5.411 FIXED-SATELLITE (Earth-to-space) MOD 5.415 MOBILE except aeronautical mobile 5.384A BROADCASTING-SATELLITE 5.347A 5.413 MOD 5.416 Earth exploration-satellite (passive) Radio astronomy Space research (passive) |
| 5.149 5.412 MOD 5.420 | 5.149 MOD 5.420 | 5.149 MOD 5.420 |
| 2 670-2 690 FIXED 5.409 5.410 5.411 MOBILE except aeronautical mobile 5.384A MOBILE-SATELLITE (Earth-to-space) 5.351A Earth exploration-satellite (passive) Radio astronomy Space research (passive) | 2 670-2 690 FIXED 5.409 5.411 FIXED-SATELLITE (Earth-to-space) (space-to-Earth) 5.347A MOD 5.415 MOBILE except aeronautical mobile 5.384A MOBILE-SATELLITE (Earth-to-space) 5.351A Earth exploration-satellite (passive) Radio astronomy Space research (passive) | 2 670-2 690 FIXED 5.409 5.411 FIXED-SATELLITE (Earth-to-space) MOD 5.415 MOBILE except aeronautical mobile 5.384A MOBILE-SATELLITE (Earth-to-space) 5.351A Earth exploration-satellite (passive) Radio astronomy Space research (passive) |
| 5.149 5.412 MOD 5.419 MOD 5.420 | 5.149 MOD 5.419 MOD 5.420 | 5.149 MOD 5.419 5.420 5.420A |

MOD	EUR/10A9/35.403	Subject to agreement obtained under No. 9.21, the band 2 520-2 535 MHz may also be used for the mobile-satellite (space-to-Earth), except aeronautical mobile-satellite, service for operation limited to within national boundaries. The provisions of No. 9.11A apply.

MOD	EUR/10A9/4

5.414	The allocation of the frequency band 2 500-2 520 MHz to the mobile-satellite service (space-to-Earth) is subject to coordination under No. 9.11A.

MOD	EUR/10A9/5

5.415	The use of the bands 2 500-2 690 MHz in Region 2 and 2 500-2 535 MHz and 2 655-2 690 MHz in Region 3 by the fixed-satellite service is limited to national and regional systems, subject to agreement obtained under No. 9.21, giving particular attention to the broadcasting-satellite service in Region 1.

MOD	EUR/10A9/6

5.416	The use of the band 2 520-2 670 MHz by the broadcasting-satellite service is limited to national and regional systems for community reception, subject to agreement obtained under No. 9.21. The provisions of No. 9.19 shall not apply to this band.     (WRC-07)

MOD	EUR/10A9/7

5.419	When introducing systems of the mobile-satellite service in the band 2 670-2 690 MHz, administrations shall take all necessary steps to protect the satellite systems operating in this band prior to 3 March 1992. The coordination of mobile-satellite systems in the band shall be in accordance with No. 9.11A.

MOD	EUR/10A9/8

5.420	The band 2 655-2 670 MHz may also be used for the mobile-satellite (Earth-to-space), except aeronautical mobile-satellite, service for operation limited to within national boundaries, subject to agreement obtained under No. 9.21. The coordination under No. 9.11A applies.

Reasons:

–	Footnotes Nos. 5.403, 5.414, 5.419 and 5.420 of Article 5 are updated to suppress the transitional effects that will be out of date at WRC-07.

–	Footnote No. 5.415 of Article 5 is updated as the limits in Table 21-4 apply, irrespective of whether they are mentioned in a footnote to Article 5. Therefore, their mention in this footnote is considered redundant and unnecessary.

ARTICLE  21

Terrestrial and space services sharing frequency bands above 1 GHz

Section V  –  Limits of power flux-density from space stations

MOD	EUR/10A9/9

TABLE  21-4     (WRC-07)

| Frequency band | Service* | Limit in dB(W/m2) for angles of arrival () above the horizontal plane | Reference bandwidth |
| --- | --- | --- | --- |
|  |  | 0-5 | 5-25 | 25-90 |  |
| . . . |
| 2 500-2 690 MHz 2 520-2 670 MHz 2 500-2 516.5 MHz (No. 5.404) 2 500-2 520 MHz 2 520-2 535 MHz (No. 5.403) | Fixed-satellite Broadcasting-satellite Radiodetermination-satellite Mobile-satellite Mobile-satellite (except aeronautical mobile-satellite) | –133 21 | –133 + 8/20(( − 5) 21 | –125 21 | 1 MHz |
| . . . |

21	21.16.19	In the 2 500-2 690 MHz band, these limits do not apply to emissions of any space station of a system in the fixed-satellite service, broadcasting-satellite service, radiodetermination-satellite service and mobile satellite-service for which complete notification information has been received by the Radiocommunication Bureau before 17 November 2007, and whose frequency assignments in the 2 500-2 690 MHz band were brought into use by 31 December 2008. In that case, the following limits shall apply:

–152			dB(W/m2)	for		    5°

–152 + 0.75( – 5)  	dB(W/m2)	for	5°  ≤	  ≤  25°

–137			dB(W/m2)	for		    25°

in any 4 kHz band, where  is the angle of arrival above the horizontal plane.     (WRC-07)

Reasons:	Europe proposes to define power flux-density (pfd) limits in Article 21 applicable to all space services, except BSS (sound) subject to No. 5.417A and No. 5.418, having an allocation in the frequency band 2 500-2 690 MHz, therefore Table 21-4 of Article 21 is updated to include bands and services not already listed. These new limits are proposed to be applicable from 17 November 2007. Transitory measures are added.

APPENDIX  5  (Rev.WRC-03)

Identification of administrations with which coordination is to be effected or 
agreement sought under the provisions of Article 9

TABLE  5-1     (Rev.WRC-03)

Technical conditions for coordination
(see Article 9)

MOD	EUR/10A9/10

TABLE  5-1 (continued)     (Rev.WRC-07)

| Reference of Article 9 | Case | Frequency bands (and Region) of the service for which coordination is sought | Threshold/condition | Calculation method | Remarks |
| --- | --- | --- | --- | --- | --- |
| … |
| No. 9.19 Terrestrial, GSO, non-GSO/ GSO, non-GSO | Any transmitting station of a terrestrial service or a transmitting earth station in the FSS (Earth-to-space) in a frequency band shared on an equal primary basis with the BSS, with respect to typical earth stations included in the service area of a space station in the BSS | Bands listed in No. 9.11, except the band 2 535-2 655 MHz, and the band 11.7-12.7 GHz | i) Necessary bandwidths overlap; and ii) the power flux-density (pfd) of the interfering station at the edge of the BSS service area exceeds the permissible level | Check by using the assigned frequencies and bandwidths | See also Article 6 of Appendix 30 |
| … |

MOD	EUR/10A9/11

TABLE  5-2 (continued)     (WRC-07)

| Frequency band (MHz) | Terrestrial service to be protected | Coordination threshold values |
| --- | --- | --- |
|  |  | GSO space stations | Non-GSO space stations |
|  |  | pfd (per space station) calculation factors (NOTE 2) | pfd (per space station) calculation factors (NOTE 2) | % FDP (in 1 MHz) (NOTE 1) |
|  |  | P | r dB/ degrees | P | r dB/ degrees |  |
| . . . |
| . . . |

Reasons:	Europe proposes to define power flux-density (pfd) limits in Article 21 applicable to all space services, except BSS (sound) subject to No. 5.417A and No. 5.418, having an allocation in the frequency band 2 500-2 690 MHz. Therefore Table 5-2 of Appendix 5 is updated with suppression of the coordination thresholds in the band 2 500-2 535 MHz, as, in accordance with No. 9.6.3, No. 9.14 will no longer apply in this band.

ARTICLE 59

Entry into force and provisional application 
            of the Radio Regulations     (WRC-2000)

MOD	EUR/10A9/12

59.1		These Regulations, which complement the provisions of the Constitution and Convention of the International Telecommunication Union, and as revised and contained in the Final Acts of WRC-95, WRC-97, WRC-2000, WRC-03 and WRC-07 shall be applied, pursuant to Article 54 of the Constitution, on the following basis.     (WRC-07)

…

ADD	EUR/10A9/13

59.9		The other provisions of these Regulations, as revised by WRC-07, shall enter into force on [1 January 2009], with the following exceptions:     (WRC-07)

ADD	EUR/10A9/14

59.10	–	the revised provisions for which other effective dates of application are stipulated in Resolutions:

..., New  Resolution [XXX] (WRC-07).     (WRC-07)

Reasons:	It is proposed that the new provisions to be decided under Agenda item 1.9 enter into force from 17 November 2007. A reference to a WRC Resolution is therefore required in Article 59.

ADD	EUR/10A9/15

draft  RESOLUTION  [EUR/10A9/15]  (WRC-07)

Provisional application of certain provisions of the
Radio Regulations as revised by WRC-07

The World Radiocommunication Conference (Geneva, 2007),

considering

a) 	that this Conference has adopted a partial revision to the Radio Regulations (RR) in accordance with its terms of reference which will enter into force on [1 January 2009];

b)	that some of the provisions, as amended by this Conference, need to apply provisionally as of an earlier date;

c) 	that as a general rule, new and revised Resolutions and Recommendations enter into force at the time of signing of the Final Acts of a Conference;

d) 	that as a general rule, Resolutions and Recommendations which a WRC has decided to suppress are abrogated at the time of the signing of the Final Acts of the Conference,

resolves

1	that, as of 17 November 2007, the following provisions of the RR, as revised or established by this Conference, shall provisionally apply: Nos. 5.403, 5.414, 5.415, 5.416, 5.419, 5.420, 21.16.19, Table 21-4, Table 5-2 of Appendix 5.

Reasons: 	It is proposed that the new provisions to be decided under Agenda item 1.9 enter into force from 17 November 2007.

______________