| XV MEETING OF PERMANENT CONSULTATIVE COMMITTEE II: RADIOCOMMUNICATIONS INCLUDING BROADCASTING November 30 to December 3, 2010 Bogata, Columbia | OEA/Ser.L/XVII.4.2 CCP.II-RADIO/doc. xxxx/10 05 October 2010 Original: English |
| --- | --- |
|  | WRC-12 AGENDA ITEM 1.11 USA proposals for the work of the conference |  |
|  | (Item on the Agenda: 4.1 (SGT2)) |  |
|  | (Document submitted by the delegation of United States of America) |  |

Agenda Item 1.11:  to consider a primary allocation to the space research service (Earth-to-space) within the band 22.55-23.15 GHz, taking into account the results of ITU-R studies, in accordance with Resolution 753 (WRC-07)

Background Information:  Downlink (space-to-Earth) transmissions will operate in the 25.5-27.0 GHz space research service (SRS) allocation to support the SRS missions in near Earth orbit, including missions in transit to the moon and at or near the moon.  Countries will use this 1.5 GHz wide downlink band for both scientific data retrieval and voice/video communication with the Earth.  However, there is a need for a companion uplink (Earth-to-space) band to provide the mission data, voice/video communications, and command and control links to support manned and unmanned missions.  The proposed SRS allocation at 23 GHz will fulfill this need for the global space science community.

Space agencies throughout the world require 600 MHz of uplink spectrum due to the potential for many concurrent exploration-related systems, the large bandwidth requirements for these systems, synergistic operations with existing data relay systems, selection of frequencies due to ranging constraints, and the evolution, growth, and complexity of those systems over a period of 20-30 years.

1)  Space agencies require their own segments of spectrum for lunar and many Lagrangian missions since antenna discrimination is not possible.  Any spacecraft around the moon and some of those with small orbit apogees around the L1 or L2 points can be situated within the main-beam lobe of other space agency antennas.

2)  The specific RF carrier frequencies selected will often be coupled with internationally agreed channels for data relay systems in order to provide global support either via an earth station or via a data relay satellite.  These data relay channels have a spacing of 60 MHz, irrespective of the actual bandwidth.

3)  There is a fixed turn-around ratio required between the Earth-to-space link around 23 GHz and the corresponding space-to-Earth link in the 25.5-27 GHz band.  This is required for ranging purposes and further limits the choice of available frequencies as it requires a suitable available companion frequency around 26 GHz.

Proposals from a number of administrations to WRC-07 covered the entire band 22.55 – 23.55 GHz.  However, compatibility concerns expressed at WRC-07 with respect to the existing HIBLEO-2 system that operates above 23.18 GHz led to a compromise that limited the bandwidth under consideration to 600 MHz.

Considering the inherently limited number of these large SRS earth stations and their remote locations, ITU-R sharing studies between SRS (Earth-to-space) and the fixed, inter-satellite and mobile services in the 22.55-23.55 GHz band determined that sharing between a new SRS (Earth-to-space) allocation in the 22.55-23.15 GHz band and the existing services in the 22.55-23.55 GHz band is feasible and will not cause harmful interference to their existing operations.

Proposal:

ARTICLE 5

Frequency allocations

Section IV – Table of Frequency Allocations

(See No. 2.1)

MOD	USA/AI1.11/1

22-24.75 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 22.55-23.15 FIXED INTER-SATELLITE 5.338A MOBILE SPACE RESEARCH SERVICE (Earth-to-space) 5.A111 5.149 |
| 23.15-23.55 FIXED INTER-SATELLITE 5.338A MOBILE 5.149 |

Reasons:   To provide a needed companion uplink (Earth-to-space) band for the transmission of mission data and command and control links for future space missions.

ADD	USA/AI1.11/2

5.A111	Unless otherwise agreed by neighboring administrations, space research service earth stations shall maintain a separation distance of at least 54 km from respective border(s) to protect the existing and future deployment of fixed and mobile services.

Reasons:   To provide a footnote regarding the location of SRS earth stations to protect existing and future deployment of FS and MS of neighboring administrations.

ARTICLE  21

Terrestrial and space services sharing frequency bands above 1 GHz

Section III  –  Power limits for earth stations

MOD	USA/AI1.11/3

TABLE  21-3  (end )     (WRC-12)

| Frequency band | Services |
| --- | --- |
| 17.7-18.1 GHz |  | Fixed-satellite |
| 22.55-23.15 GHz 27.0-27.5 GHz6 | (for Regions 2 and 3) | Earth exploration-satellite Mobile-satellite |
| 27.5-29.5 GHz |  | Space research |
| 31.0-31.3 GHz | (for the countries listed in No. 5.545) |  |
| 34.2-35.2 GHz | (for the countries listed in No. 5.550 with respect to the countries listed in No. 5.549) |  |

Reasons:  The band 22.55-23.15 GHz is added to Table 21-3 to ensure protection of terrestrial services consequential to the addition of the SRS uplink allocation.

SUP	USA/AI1.11/4

RESOLUTION 753  (WRC-07)

Use of the band 22.55-23.15 GHz by the space research service

Reasons:  Required studies have been completed for this agenda item; no more work is needed.