## Slide 1: Working Group 9: Wi-Fi Security Status Update
September 14, 2016
Brian K. Daly, AT&T

## Slide 2: TOPICS
Brief WG9 Background
  Including Objectives, Deliverables, Membership
Status update
Next Steps

## Slide 3: WG9 Objectives & Deliverable
Working Group Description:
WG9 will develop, for CSRIC’s consideration, recommended best practices for promoting security in networks and devices utilizing Wi-Fi spectrum bands.
Security concerns threaten entities utilizing Wi-Fi devices and spectrum. Currently, enterprises utilizing Wi-Fi spectrum rely on numerous methods to secure their networks and connected devices from malicious attacks.
Working Group 9 will identify, for CSRIC’s consideration when, and under what circumstances, the use of a variety of advanced security techniques are appropriate.
Specifically the Working Group will identify, for CSRIC’s consideration:
  The threats most consistently facing Wi-Fi network operators and users;
  The available security techniques to prevent and/or remediate the threats;
  The extent to which each technique is effective against specific threats, avoids interference with legitimate activity, is easily deployed, and is currently deployed.
Working Group Deliverable:
Prepare and present recommended security best practices for Wi-Fi operators, users, and consumers. – March 2017

## Slide 4
WG9 Chair:
  Brian K. Daly, AT&T
FCC Liaisons:
  Peter Shroyer
  Kurian Jacob
WG Editor
  DeWayne Sennett, AT&T
NAME | COMPANY/AFFILIATION
Paul Hancock | AT&T Services, Inc.
Robert Mayer | USTelecom Association
Phil Levis | Stanford
Jon Green | Aruba
Mohammad Khaled | Nokia
Stephen Orr | Cisco
Bing Yang | Uconn
Miles Green | Intersection (LinkNYC)
David Savage | Boeing
Pat Walsh | Gogo Inflight
Joe McManus | CU Boulder
Craig Cowden | Charter Communications
Jesse Walker | Intel
Jose Jiminez | Cox
Brian Scarpelli | ACT
Scott Craighead | IAEE
Sameer Khan | Sprint
Mark S. Sims | Javits Convention Center
Mark Haley | Smart City
Brad Mayne | International Association of Venue Management
WG9 Membership

## Slide 5
Work in progress on the deliverable
  Outline developed
  Contributions and discussions
    Biweekly calls
    Email discussions
  Discussion include:
    Use Cases & potential Wi-Fi Security Threats
    Identifying Potential Wi-Fi Adversaries
    Wi-Fi Adversaries Can Inflict Damage Against a System
    Observations on Wi-Fi Compromises
WG9 Status

## Slide 6
1 Results in Brief
  1.1 Executive Summary
2 Introduction
  2.1 CSRIC Structure
  2.2 Working Group 9 Team Members
3 Objective, Scope, and Methodology
  3.1 Objective
  3.2 Scope
  3.3 Methodology
4 Current Security Weaknesses in Wi-Fi
  4.1 Wi-Fi Threats Discussion Paper
  4.1.1 Background and Context
  4.1.2 Wi-Fi Threats
  4.1.3 Discussion
5 Definition of Potential Wi-Fi Security Threats
6 Use Cases & Threats Most Consistently Facing Wi-Fi Network Operators and Users
  6.1 In-Home Wi-Fi Network Use Case
  6.2 In-Vehicle Wi-Fi Network Use Case
  6.3 In-Flight Wi-Fi Network Use Case
  6.4 Public Municipal Wi-Fi Network Use Case
  6.5 Commercial Subscription/Fee-Based Wi-Fi Network Use Case
  6.6 Hotel Wi-Fi Network Use Case
  6.7 Convention Center/Public Venue Wi-Fi Network Use Case
  6.8 Private Enterprise Network Use Case
  6.9 Use Cases for Connected IoT Devices
  6.9.1 Connected Home IoT Devices Use Case
  6.9.2 Wearable IoT Devices Use Case
  6.9.3 Connected Medical IoT Devices Use Case
WG9 Draft Deliverable Outline

## Slide 7
7 Summary of Threats Most Consistently Facing Wi-Fi Network Operators and Users
8 Security Technique Effectiveness, Interference, Ease of Deployment, & Deployment Status
9 End User Experience with Wi-Fi Security
10 Conclusions
11 Recommended Security Best Practices for Wi-Fi Operators, Users, and Consumers
Appendix A: Summary of CSRIC WG2A Cyber Security Best Practices Report
Appendix B: Summary of NIST Establishing Wireless Robust Security Networks Report
Appendix C: Suggested Background Reading
Appendix D: Acronyms
Appendix E: References
Revision History
WG9 Draft Deliverable Outline

## Slide 8: WG9 Initial Discussions
Wi-Fi specifications call for a Wi-Fi device to send messages to another by broadcasting over a radio channel, with the goal of emulating a point-to-point link between the two
However, any other radio receiver listening on the same broadcast channel can receive the message
  behavior that is not intended by the Wi-Fi specification
An easy attack against unsecured Wi-Fi is to utilize this unintended behavior to eavesdrop on messages exchanged among devices
Off-the-shelf, easy-to-use, and low-cost tools exist to launch attacks against Wi-Fi confidentiality, integrity, and availability
Given the relative ease of launching successful attack against a Wi-Fi network that has not been secured against integrity and confidentiality threats, it seems prudent to utilize Wi-Fi security mechanisms as much as possible
The locality constraint on Wi-Fi attacks makes it difficult for a criminal enterprise to build a global business model based exclusively on Wi-Fi vulnerabilities, so we should expect attacks against Wi-Fi should be opportunistic and at most one tool inside a larger attacker tool set

## Slide 9: WG9 Initial Discussions
WG defining Use Cases & potential Wi-Fi Security Threats:
Potential Threats:
  Ad Hocs and Soft APs
  AP Security including software
  Data Interception
  Denial of Service
  Endpoint Attacks
  Evil Twin
  Hack into Other Systems via Wi-Fi
  Malware Distribution
  Man in the Middle
  Misbehaving Clients
  Misconfigured APs
  Multiple Domain Issue
  Misuse of Wi-Fi networks for threatening or intimidation reasons
  Privacy
  Rogue APs
  Wireless Intruders
  Wireless Phishing
Use Cases:
  In-Home Wi-Fi Network Use Case
  In-Vehicle Wi-Fi Network Use Case
  In-Flight Wi-Fi Network Use Case
  Public Municipal Wi-Fi Network Use Case
  Commercial Subscription/Fee-Based Wi-Fi Network Use Case
  Hotel Wi-Fi Network Use Case
  Convention Center/Public Venue Wi-Fi Network Use Case
  Private Enterprise Network Use Case
  Use Cases for Connected IoT Devices
  Connected Home IoT Devices Use Case
  Wearable IoT Devices Use Case
  Connected Medical IoT Devices Use Case

## Slide 10: Identifying Potential Wi-Fi Adversaries
WORK IN PROGRESS
Adversaries with different kinds of skills are able to attack a system in different ways:
Network adversary
  Eavesdrop on any message sent over a communications channel, alter messages, inject messages, delay messages, reorder messages, mis-deliver messages, and delete messages.
Software adversary
  Read from and write to the memory of running software, both code and data, and can alter both program control flow and data in arbitrary ways. This includes the ability to observe program state changes, reverse engineer the software, thereby revealing all of its functionality to the attacker.
Simple Hardware adversary
  Can add, remove, or replace components on a motherboard, can monitor and inject data and control exchanged between components, control the electrical and thermal characteristics of system’s environment, reflash BIOS and other firmware, and the like. A simple hardware adversary can, in short, transform an existing hardware platform into something with completely new capabilities and limitations.
Sophisticated hardware adversary
  Can monitor and reverse engineer operating silicon components, and can also cause the silicon components to operate outside of their specifications. Such an adversary can steal cryptographic keys from “secure” hardware and fundamentally alter the operation of any part.
Supply chain adversary
  Can inject backdoors and other weaknesses into components or software during design and manufacturing, and steal trade secrets and other proprietary information about how components and software are designed, manufactured, and function, information which other types of adversaries can consume to compromise deployed systems.
Administrative adversary
  Consists of authorized personnel (aka “insiders”) who abuse their position by deploying, operating, or maintaining a system in a way that is outside of established policy. They can thereby illegally obtain personal information about system users, proprietary information about the organization using the system, mis-use the system for personal gain or revenge, etc.
Social engineering adversary
  Can exploit human relationships to gain unauthorized access to system resources. A classical social engineering attack is to simply ask a user for a password or some other access token, as a non-negligible percentage of user will comply with the request.

## Slide 11: Wi-Fi Adversaries Can Inflict Damage Against a System
WORK IN PROGRESS
Any one of our adversary models can inflict three types of damage against a system:
Confidentiality compromises
  The adversary can conduct unauthorized eavesdropping on data and control flows, to learn information about the system or its data which is not intended. This corresponds to a network adversary’s assumed ability to eavesdrop on communications
Integrity compromises
  The adversary can inject unauthorized data and control into the system, and modify legitimate data and control flows, to make the system act contrary to its purpose. This corresponds to a network adversary’s assumed ability to alter, inject, delay, reorder, and mis-deliver messages
Availability compromises
  The adversary can disrupt the services the system provides. This corresponds to a network adversary’s assumed ability to delete messages from a communications channel.

## Slide 12: Observations on Wi-Fi Compromises
WORK IN PROGRESS
Wi-Fi enhances a network adversary’s ability to accomplish all three types of compromises:
  Anyone with a radio receiver tuned to the right frequency and within about 100 meters of a Wi-Fi transmitter can capture messages sent over the channel.
  Anyone with a radio transmitter and within about 100 meters of a Wi-Fi receiver can send messages on the channel.
  Anyone with a radio transmitter can jam a Wi-Fi channel used by other devices within about 100 meters.
Many non-security professionals rank the threat against Wi-Fi’s confidentiality as the one requiring the most urgent attention
  Wi-Fi uses encryption to provide confidentiality, but encryption provides no integrity protection, and is more easily compromised by active attackers who create message forgeries than by a passive listener
Maintaining message integrity is the central design goal for Wi-Fi security, with confidentiality a secondary goal, and denial-of-service mitigation may not be a goal at all
  Defending against denial-of-service has never been viewed as a practical problem, as launching a jamming attack has a low-cost, and the known message integrity mechanisms intentionally transform forgery attacks into denial-of-service attacks
  Existing Wi-Fi devices are often mobile, and so can be moved away from a jamming source, and can then reconnect when they come within range of an access point whose signal strength is stronger than the jammer’s.
  It is reasonably easy to locate and then disable a jamming device
Neither the “flight” nor the “search-and-destroy” strategy may work with some types of Internet of Things applications

## Slide 13: WG9 Next Steps
Continue work to accomplish the CSRIC V mission, based on WG9 members’ subject matter expertise
Continue working group calls
Continue email discussions
Provide periodic status updates to Steering Committee and Council
Delivering final report in March 2017

## Slide 14
Thank You
Questions??